## Slide 1: McStas - Mantid
Torben Nielsen
Anders Markvardsen
Peter Willendrup
www.europeanspallationsource.se
28 April, 2017

## Slide 2: Outline
Motivation
Illustration of the Mantid-McStas interface
  A simple toy model: templateSANS.instr
TOF, IDF, and NeXus files
How to use – a little more explanation
Demo time
A few other examples

## Slide 3: Motivation: I - Highlevel
Mantid is well established software – long history
McStas is well established software – long history
Wanted to combine the reduction framework and the neutron transport framework
So users can seeming less do transport, reduction and “analysis” in one go

## Slide 4: Motivation: II - Benefits for users
View McStas data in Mantid (simple – but nice to have)
Import McStas event data to Mantid
Use already developed and tested algorithms in Mantid to process McStas event data (no need to reinvent stuff!!!)
Advanced use: Use McStas to quantify (perhaps remove) “spurries” signal on detector (can scatt. – multi. scatt )

## Slide 5: Illustration: simplified SANS instrument

## Slide 6: McStas GUI: templateSANS
R=150,phi=0.1, d=1,a=0

## Slide 7: Mantid GUI: templateSANS McStas data

## Slide 8: How to use: TOF and pixel ID’s
Mantid was designed for data reduction at TOF spallation neutron sources
Mantid’s IDF store geometry information use in TOF analysis
This implies parsing information about:
  where the neutron source is located,
  where the sample is located,
  where each individual detector pixel is located.

## Slide 9: How to use: NeXus file
NeXus file
Mantid
The McStas Nexus file must contain:
Event data, i.e each neutron has a pixel id and a time stamp
An IDF McStas monitor_nD gives pixle id & time for each event
mcdisplay can auto-generate an IDF

## Slide 10: How to use: McStas NeXus file
Event data
IDF xml data

## Slide 11: How to use: Online documentation
Buil-in Mantid
Github McStas
Archive - lanl.arXiv.org

## Slide 12: How to use: McStas event conventions
McStas instrument file name and the McStas defined name of the instrument must be the same:
E.g. templateSANS_Mantid.instr and “DEFINE INSTRUMENT templateSANS_Mantid(…. )”
In the McStas instrument file the source must be named “sourceMantid”
E.g. "COMPONENT sourceMantid = Source_simple(…. )"
In the McStas instrument file the sample must be named “sampleMantid”
E.g. "COMPONENT sampleMantid = Sans_spheres(…. )"
In the McStas instrument file the event monitors must be named “nD_Mantid_#”
E.g. "COMPONENT nD_Mantid_1 = Monitor_nD(…. )"

## Slide 13: How to use: Generate the IDF
How-to generate McStas event data for Mantid
Step 1. Generate IDF:
mcdisplay templateSANS_Mantid.instr --format=Mantid -n0
A new xml IDF file is then generated on disk

## Slide 14: McStas – Mantid: Demo Time
See how to use Mantid – McStas interface

## Slide 15: Examples of detectors: IN5 (ILL) and LoKI (ESS)

## Slide 16: Example of real data: SANS2D
Mantid view of the McStas event data generated for the ISIS_SANS2d.instr file.
Comparison of rescaled scatting intensity I(q) derived from the experimental data and a McStas simulation. Nanospheres of radius 150 Å, polydispersion 0.2.

## Slide 17: Example: Usage of Mantid algorithms
McStas – Mantid
2D scattering kernel from SasView
2D reduction in Mantid: Qxy
Can be send back to SasView fitting

## Slide 18
The end …....

## Slide 19: How to use: Make NeXus file for Mantid
How-to generate McStas event data for Mantid
Step 1. Compile c code:
gcc -o templateSANS_Mantid.out templateSANS_Mantid.c -DUSE_NEXUS –lNeXus –lm
Step 2. Run simulation:
templateSANS_Mantid.out --format=Nexus
Now IDF is embedded in the NeXus file to be read by Mantid

## Slide 20: Example: Single_crystal
Use exercise “Single_crystal” to transform instrument file to be read from Mantid