## Slide 1
Sources and Monitors
McStas monitors & sources
Monitors & Sources

## Slide 2: Access the docs
In this session:
Overview of existing Source and Monitor components
Detailed description of the most commonly used ones
How to ‘call’ them into a *.instr file
Practical Exercise using sources and monitors
IMPORTANT:
All (and more) of this information can be found in the online pdf component documentation, e.g.
http://www.mcstas.org/documentation/manual/mcstas-2.3-components.pdf
- is also distributed with your McStas installation - mcdoc -c
The component documentation along with the “mcdoc component_you_are_searching_for” command, are your best friends when using McStas
Sources and Monitors

## Slide 3: Sources
Mathematical:
  Source_simple.comp
  Source_div.comp
Pulsed sources:
  ESS_moderator.comp
  Moderator.comp
  SNS_source.comp (*)
  ISIS_moderator.comp (*)
Sources and Monitors
(*) contributed (can be found in /mcstas/installation/folder/contrib )
Reactors :
  Source_Maxwell_3.comp
  Source_gen.comp
  Source_gen4.comp
  Source_multi_surfaces.comp (*)

## Slide 4: Sources
Sources and Monitors
(*) contributed (can be found in /mcstas/installation/folder/contrib )
Typing “mcdoc”, mcdoc source” or “mcdoc moderator” in your command shell, will reveal a list of available sources and moderators.
Or you can search in the directories ‘sources’, ‘contrib’, and ‘obsolete’.

## Slide 5: Sources
Sources and Monitors
(*) contributed (can be found in /mcstas/installation/folder/contrib )
Typing “mcdoc”, mcdoc source” or “mcdoc moderator” in your command shell, will reveal a list of available sources and moderators.
Or you can search in the directories ‘sources’, ‘contrib’, and ‘obsolete’.
Steady-state sources
(Reactors & PSI… )

## Slide 6: Sources
Sources and Monitors
(*) contributed (can be found in /mcstas/installation/folder/contrib )
Typing “mcdoc”, mcdoc source” or “mcdoc moderator” in your command shell, will reveal a list of available sources and moderators.
Or you can search in the directories ‘sources’, ‘contrib’, and ‘obsolete’.
Pulsed sources
(also SNS_source and ISIS_moderator in the contrib category)

## Slide 7: Sources
Source_simple.comp
What do we need the distance and target size for?
(let us take a small break and investigate this)
Sources and Monitors
A Simple continuous source with flat energy/wavelength spectrum

## Slide 8: Sources
Sources and Monitors

## Slide 9: Sources
Sources and Monitors

## Slide 10: Source_simple
Example:
COMPONENT my_simple_source = Source_simple(radius=0.1, dist=2.0,
focus_xw=0.1, focus_yh=0.1, E0=14.0,
dE=2.0)
Sources and Monitors
Source_simple.comp
A Simple continuous source with flat energy/wavelength spectrum

## Slide 11: Monitor output PSD / Emon
Sources and Monitors
Source_simple.comp
A Simple continuous source with flat energy/wavelength spectrum

## Slide 12: Monitor output PSD / Emon
Sources and Monitors
Source_simple.comp
gauss = 1
A Simple continuous source with flat energy/wavelength spectrum

## Slide 13: Source_div
Sources and Monitors
Example:
COMPONENT my_source_div = Source_div(xwidth=0.1, yheight=0.1,
    focus_aw=2,focus_ah=2, E0=14, dE=2, gauss=0)
Source_div.comp
A Simple continuous source with flat energy/wavelength spectrum

## Slide 14: Source_div
Sources and Monitors
Source_div.comp
A Simple continuous source with flat energy/wavelength spectrum

## Slide 15: Source_div
Sources and Monitors
Source_div.comp
gauss = 1
A Simple continuous source with flat energy/wavelength spectrum

## Slide 16: Source_gen
Sources and Monitors
Example:
COMPONENT my_source_gen = Source_gen(yheight=0.1, xwidth=0.1, Emin=1,
                Emax=3, I1=1e13, verbose=1, focus_xw=0.01,
                focus_yh=0.01)
Source_gen.comp
A general continuous source

## Slide 17: Source_gen
Sources and Monitors
Example:
COMPONENT my_source_gen = Source_gen(yheight=0.1, xwidth=0.1,
dist=1.5, focus_xw=0.01, focus_yh=0.01,
lambda0=1, dlambda=8,
flux_file=‘source.dat’)
Source_gen.comp
A general continuous source
Source input can be an ASCII file!!

## Slide 18: Source_Maxwell 3 ~ Source_gen
Source_Maxwell_3.comp
A continuous source with a maxwellian spectrum
Sources and Monitors

## Slide 19: Source_Maxwell_3
Source_Maxwell_3.comp
Sources and Monitors
COMPONENT source = Source_Maxwell_3(yheight=0.156, xwidth=0.126,
Lmin=0.1, Lmax=9.0, dist=1.5, focus_xw = 0.025,
focus_yh = 0.12, T1=296.16, I1=8.5E11,
              T2=40.68, I2=5.2E11)
A continuous source with a maxwellian spectrum

## Slide 20: Special sources
Special Sources
“Feedback” components:
      Adapt_check.comp
      Source_adapt.comp
      Source_Optimizer.comp
      Monitor_Optimizer.comp
I/O mechanisms:
      Virtual_input.comp
      Virtual_output.comp
      Virtual_mcnp_ss_input.comp
      Virtual_tripoli4_input.comp
      Virtual_mcnp_ss_output.comp
      Virtual_tripoli4_output.comp
      Vitess_input.comp
      Vitess_output.comp
      MCPL_input.comp (useful for MCNP/McStas coupling (*))
      MCPL_output.comp (useful for MCNP/McStas coupling (*))
Sources and Monitors
(*) Kittelmann, et. al (2017) https://arxiv.org/abs/1609.02792

## Slide 21: Special sources
Special Sources
“Feedback” components:
      Adapt_check.comp
      Source_adapt.comp
      Source_Optimizer.comp
      Monitor_Optimizer.comp
I/O mechanisms:
      Virtual_input.comp
      Virtual_output.comp
      Virtual_mcnp_ss_input.comp
      Virtual_tripoli4_input.comp
      Virtual_mcnp_ss_output.comp
      Virtual_tripoli4_output.comp
      Vitess_input.comp
      Vitess_output.comp
      MCPL_input.comp (useful for MCNP/McStas coupling (*))
      MCPL_output.comp (useful for MCNP/McStas coupling (*))
Sources and Monitors
(*) Kittelmann, et. al (2017) https://arxiv.org/abs/1609.02792
Need more practical info on that?
Ask the instructors (could say something on friday)

## Slide 22: Monitors
Sources and Monitors

## Slide 23: Monitors
Sources and Monitors
Semantics
In reality:
    Monitor: intensity probe of the beam; transparent to neutrons; has efficiency <1%
    Detector: should detect each and every neutron; as high efficiency as possible.
In McStas:
    In simulations we can program monitors and detectors to behave any way we like. We refer to both of those indistinguishably as ‘monitors’.
      (With exception of PSD_Detector that models a “physical” He3 detector)

## Slide 24: L_monitor
Sources and Monitors
L_monitor.comp
1-D wavelength sensitive monitor
Example:
COMPONENT my_L_monitor = L_monitor(xmin=-0.1, xmax=0.1, ymin=-0.1,
ymax=0.1, nL=20, filename="Output.L",
Lmin=2, Lmax=10)

## Slide 25: L_monitor
Sources and Monitors
L_monitor.comp
1-D wavelength sensitive monitor

## Slide 26: L_monitor
Sources and Monitors
L_monitor.comp
1-D wavelength sensitive monitor
“Intensity” n/s
Statistical RMS variance on intensity
# neutron rays / events recorded
Signal stats, mean & spread wl

## Slide 27: L_monitor
Sources and Monitors
L_monitor.comp
1-D wavelength sensitive monitor
“Intensity” n/s
Statistical RMS variance on intensity
# neutron rays / events recorded
Signal stats, mean & spread wl
Same info available “pr. bin”

## Slide 28: PSD_monitor
Sources and Monitors
PSD_monitor.comp
2-D position sensitive monitor
Example:
COMPONENT my_PSD_monitor = PSD_monitor(xmin=-0.1, xmax=0.1, ymin=-0.1
                ymax=0.1, nx=90, ny=90,
                filename="Output.psd")

## Slide 29: PSD_monitor
Sources and Monitors
PSD_monitor.comp
2-D position sensitive monitor
Example:
COMPONENT my_PSD_monitor = PSD_monitor(xmin=-0.1, xmax=0.1, ymin=-0.1
                ymax=0.1, nx=90, ny=90,
                filename="Output.psd")

## Slide 30: More monitors
Sources and Monitors
More Monitors
      TOF_monitor.comp
      E_monitor.comp (1-D energy sensitive monitor)
      Res_monitor.comp
      TOFLambda_monitor.comp (2-D TOF vs. wavelength monitor)
      Divergence_monitor.comp (2-D divergence monitor)
      EPSD_monitor.comp
      DivPos_monitor.comp (2-D divergence and position monitor)
      Brilliance_monitor.comp
      DivLambda_monitor.comp
      Monitor.comp
      Hdiv_monitor.comp
      PSDlin_monitor.comp
      PSD_monitor_4PI.comp
      Monitor_Sqw.comp
      Pol_monitor.comp
      Monitor_4PI.comp
      .......
      Monitor_nD

## Slide 31: More monitors
Sources and Monitors
      TOF_monitor.comp
      E_monitor.comp (1-D energy sensitive monitor)
      Res_monitor.comp
      TOFLambda_monitor.comp (2-D TOF vs. wavelength monitor)
      Divergence_monitor.comp (2-D divergence monitor)
      EPSD_monitor.comp
      DivPos_monitor.comp (2-D divergence and position monitor)
      Brilliance_monitor.comp
      DivLambda_monitor.comp
      Monitor.comp
      Hdiv_monitor.comp
      PSDlin_monitor.comp
      PSD_monitor_4PI.comp
      Monitor_Sqw.comp
      Pol_monitor.comp
      Monitor_4PI.comp
      .......
      Monitor_nD
More Monitors

## Slide 32: More monitors
Sources and Monitors
      TOF_monitor.comp
      E_monitor.comp (1-D energy sensitive monitor)
      Res_monitor.comp
      TOFLambda_monitor.comp (2-D TOF vs. wavelength monitor)
      Divergence_monitor.comp (2-D divergence monitor)
      EPSD_monitor.comp
      DivPos_monitor.comp (2-D divergence and position monitor)
      Brilliance_monitor.comp
      DivLambda_monitor.comp
      Monitor.comp
      Hdiv_monitor.comp
      PSDlin_monitor.comp
      PSD_monitor_4PI.comp
      Monitor_Sqw.comp
      Pol_monitor.comp
      Monitor_4PI.comp
      .......
      Monitor_nD
More Monitors

## Slide 33: Monitor_nD
Monitor_nD.comp
A general monitor for 0D/1D/2D records
The all-in-one , swiss-army-knife of monitors
Monitor_nD can have almost any shape, and record
any requested standard quantities
Sources and Monitors

## Slide 34: Monitor_nD
A general monitor for 0D/1D/2D records
Monitor_nD.comp

## Slide 35: Monitor_nD
A general monitor for 0D/1D/2D records
EXAMPLES:
COMPONENT MyMon = Monitor_nD( xwidth = 0.1, yheight = 0.1, zdepth = 0,
options = "intensity per cm2 angle,limits=[-5 5],
bins=10,with borders, file = mon1")
Sources and Monitors
options = "banana, theta limits=[10,130], bins=120, y"
COMPONENT MyMo = Monitor_nD(xwidth = 0.1, yheight = 0.1,
              user1=age, username1="Age of the Captain [years]",
              options="user1, auto")
options = "multiple kx ky kz, auto abs log t, and list all neutrons"
Monitor_nD.comp

## Slide 36
Mathematical:
  Source_simple.comp
  Source_div.comp
Pulsed sources:
  ESS_moderator.comp
  Moderator.comp
  SNS_source.comp (*)
  ISIS_moderator.comp (*)
Sources and Monitors
Reactors :
  Source_Maxwell_3.comp
  Source_gen.comp
  Source_gen4.comp
  Source_multi_surfaces.comp (*)
(*) contributed (can be found in /mcstas/installation/folder/contrib )

## Slide 37: A job for you…
EXERCISE 1
Create a new instrument file, named ‘sources_monitors_ex.instr’.
    HINT: you can use the ‘template.instr’ file that exists in today’s class folder and you can open it with the editor of your liking, or open it from the McStas gui by clicking either:
      File —> New (python) or
      neutron site --> Templates --> template_simple (perl)
Add a source using the Source_gen.comp component, with:
    source dimensions: (w)0.132m X (h)0.164m
    distance to target : 1.5 m
    focus area: (w)0.03m X (h)0.12m
    wavelength range: 0.1Å to 9.9Å
    T1=27.63[K], I1=2.4E12 [n/s/cm2/st/AA], T2=130.76[K],
    I2=4.03E12[n/s/cm2/st/AA] ,T3=309.33[K], I3=1.24E13[n/s/cm2/st/AA]
Add the following monitors at two different distances from the source, at 1.5m and 4.5m:
    PSD monitor (PSD_monitor)
    A linear PSD monitor for the y-direction (PSDlin_monitor)
    Wavelength monitor (L_monitor)
    2D Divergence monitor (Divergence_monitor)
    Divergence-position monitor for the x-direction (DivPos_monitor)
Sources and Monitors