## Slide 1
MERLIN
MCSTAS model
ISIS Mcstas workshop 2017
26/4/17
Rob Bewley

## Slide 2
MERLIN
A direct geometry thermal neutron spectrometer

## Slide 3
Ei fixed
sample
detectors
Time
Distance
Moderator
Nimonic
Chopper
Fermi
Chopper
Sample
Detectors
Neutron path
tdet
Ei
EF
MAPS, MERLIN, MARI and LET all examples of direct geometry TOF spectrometers
Advantages of Direct geometry;
Low backgrounds
Flexibility –fluxresolution
Large fixed detector arrays

## Slide 4
Direct geometry machines can have a very large area of position sensitive detector coverage
MERLIN and LET have  steradians solid angle
Great for mapping out the full 4D S(Q,w) mapping

## Slide 5
Most experiments on LET/MERLIN want to do HORACE scans (measure the full 4D Qx, Qy, Qz , E data set). V
4D data sets
Rotate-measure-rotate-measure
To build up 4D S(Q,w)

## Slide 6
MERLIN.instr
Write comments at top
Remind myself what the input parameters are
/* %Parameters
* INPUT PARAMETERS:
* E_min : lowest energy sampled [meV]
* E_max : highest energy sampled [meV]
* E_foc : energy selected by chopper [meV]
* nu_hz : frequency of chopper rotation [Hz]
* type : chopper package selected [sloppy chopper = 1, B chopper = 2]
* m : m value of guides
*
*******************************************************************************/

## Slide 7
MERLIN.INST
Define the instrument
The name of instrument and the input parameters
DEFINE INSTRUMENT MERLIN(E_min=1.0, E_max=2000.0, m=3.0,
E_foc=80.0,nu_hz=200.0,int type=3)

## Slide 8
MERLIN.instr
Declare any variables used
DECLARE
%{
double slit_curv,num_slits,width,len;
double lam,phase_time,t_det,t_fer;
%}

## Slide 9
MERLIN.instr
Initialize
Here I define the Fermi chopper parameters depending on chopper package ‘type’ selected
INITIALIZE
%{
if (type==1)
{slit_curv=1/0.82;
num_slits=55;
width=0.00114;
len=0.099;
fprintf(stderr,"MERLIN b chopper selected");
}
if (type==2)
{slit_curv=1/1.3;
num_slits=28;
width=0.00228;
len=0.099;
fprintf(stderr,"MERLIN Sloppy selected selected");
}
if (type==3)
{slit_curv=0;
num_slits=350;
width=0.0002;
len=0.01;
fprintf(stderr,"Merlin Gd selected selected");
}

## Slide 10
MERLIN.INST
Initialize
Define the opening time of fermi chopper
i.e time it should open to focus on energy E_foc
Also define a few other parameters
/* calculate opening time of the fermi chopper at 10m from moderator*/
phase_time = (2.28e-3*10.0/sqrt(E_foc));
printf("\nphase_time: %f\n\n",phase_time);
t_det=1.43*phase_time;
t_fer=1.02*phase_time;
lam = sqrt(81.81/E_foc);
%}

## Slide 11
TRACE
/* define origin */
COMPONENT Origin = Arm()
AT (0,0,0) ABSOLUTE
Trace is the start of the instrument components
Define an origin using the Arm()
component

## Slide 12
/* The moderator */
COMPONENT isis_mod =
ViewModISISver1(Face="TS1verBase2016_LH8020_newVM-var_South04_Merlin.mcstas", E0 = E_min, E1 = E_max,
dist = 1.7, xw = 0.094, yh = 0.094, modPosition=0,tally=8.4,modXsize=0.12,modZsize=0.12)
AT (0,0,0) RELATIVE Origin
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80

## Slide 13
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT TOF_mod= TOF_monitor(
nt = 150, filename = "mod.m",xmin = -0.025,
xmax = 0.025, ymin = -0.025, ymax = 0.025, tmin=0, tmax =150 )
AT (0, 0, 0.001) RELATIVE Origin

## Slide 14
Put E_min just below E_max
Example below E_min=79 Emax= 80 so have moderator shape for 80 meV neutrons
Getting the moderator term

## Slide 15
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT shutter_guide = Guide_channeled(
w1 = 0.094, h1 = 0.094, w2 = 0.094, h2 = 0.094, l = 2.0, alphax = 4.38, alphay = 4.38 ,
W=3e-3, mx = m, my = m)
AT (0, 0, 1.7) RELATIVE Origin

## Slide 16
* INPUT PARAMETERS:
*
* w1: (m) Width at the guide entry
* h1: (m) Height at the guide entry
* w2: (m) Width at the guide exit
* h2: (m) Height at the guide exit
* l: (m) Length of guide
* d: (m) Thickness of subdividing absorbing walls
* nslit: (1) Number of channels in the guide (>= 1)
* R0: (1) Low-angle reflectivity
* Qc: (AA-1) Critical scattering vector
* alpha: (AA) Slope of reflectivity
* m: (1) m-value of material. Zero means completely absorbing.
* W: (AA-1) Width of supermirror cut-off for all mirrors
* Qcx: (AA-1) Critical scattering vector for left and right vertical mirrors in each channel
* Qcy: (AA-1) Critical scattering vector for top and bottom mirrors
* alphax: (AA) Slope of reflectivity for left and right vertical mirrors in each channel
* alphay: (AA) Slope of reflectivity for top and bottom mirrors
* mx: (1) m-value of material for left and right vertical mirrors in each channel. Zero means completely absorbing.
* my: (1) m-value of material for top and bottom mirrors. Zero means completely absorbing.

## Slide 17
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT conv_guide = Guide_channeled(
w1 = 0.094, h1 = 0.094, w2 = 0.067, h2 = 0.067, l = 4.760, alphax = 4.38, alphay = 4.38 ,
W=3e-3, mx = m, my = m)
AT (0, 0, 3.704) RELATIVE Origin

## Slide 18
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT between_guide = Guide_channeled(
w1 = 0.0629, h1 = 0.0629, w2 = 0.0594, h2 = 0.0594, l = 0.640, alphax = 4.38, alphay = 4.38 ,
W=3e-3, mx = m, my = m)
AT (0, 0, 9.182) RELATIVE Origin

## Slide 19
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT fermi = FermiChopper(time=phase_time, radius=0.055, nu=nu_hz,
yheight=0.07, w=width ,nslit=num_slits, R0=0.0,
Qc=0.02176, alpha=2.33, m=0, length=len, eff=0.95, curvature=-slit_curv, zero_time=0)
AT (0,0,10) RELATIVE Origin

## Slide 20
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT TOF_fermi= TOF_monitor(
nt = 50, filename = "fermi.m",xmin = -0.025,
xmax = 0.025, ymin = -0.025, ymax = 0.025, tmin=(1e6*t_fer)-12, tmax =(1e6*t_fer)+22 )
AT (0, 0, 10.2) RELATIVE Origin

## Slide 21
TOF fermi
Use monitors down your beam line to check things are as they should be
E_foc = 80mev  =1.01Ǻ time= 252.82 x L x  = 2607 us

## Slide 22
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT final_Guide = Guide_channeled(
w1 = 0.0568, h1 = 0.0568, w2 = 0.0506, h2 = 0.0506, l = 1.10, alphax = 4.38, alphay = 4.38 ,
W=3e-3, mx = m, my = m)
AT (0, 0, 10.277) RELATIVE Origin

## Slide 23
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT horz_div = Hdiv_monitor(nh=30, filename="horz.div.m",
xmin=-0.025, xmax=0.025, ymin=-0.025, ymax=0.025,
h_maxdiv=0.3*lam+.4)
AT (0, 0, 11.79) RELATIVE Origin

## Slide 24
Horizontal divergence

## Slide 25
COMPONENT fermi = FermiChopper(time=phase_time, radius=0.055, nu=-nu_hz,
yheight=0.07, w=width ,nslit=num_slits, R0=0.0,
Qc=0.02176, alpha=2.33, m=0, length=len, eff=0.95, curvature=-slit_curv, zero_time=0)
AT (0,0,10) RELATIVE Origin
Reverse direction of fermi chopper

## Slide 26
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT PSD = PSD_monitor(xmin=-0.04, xmax=0.04, ymin=-0.04, ymax=0.04,
nx=20, ny=20, filename="Output.psd")
AT (0, 0, 11.795) RELATIVE Origin

## Slide 27
Check for smooth homogeneous beam
With guides and gaps/apertures can get
a structured beam

## Slide 28
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT sample = Incoherent(radius=0.02, thickness=0.001,yheight=0.04,
focus_xw=0.025, focus_yh=0.1,sigma_abs=0.0,sigma_inc=100, target_index=2)
AT (0, 0, 11.8) RELATIVE Origin

## Slide 29
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT detectorarm = Arm()
AT (0, 0, 0) RELATIVE sample
ROTATED (0,20.0,0) RELATIVE sample

## Slide 30
1.7
9.18
3.7
10.27
0
8.46
10.0
9.82
11.37
Moderator
Shutter guide
Converging guide
T0 chopper
Fermi chopper
Converging guide
Converging guide
sample
11.80
COMPONENT detector= TOF_monitor(
nt = 25, filename = "detector.m",xmin = -0.0125,
xmax = 0.0125, ymin = -0.05, ymax = 0.05, tmin=(1e6*t_det)-20, tmax =(1e6*t_det)+30)
AT (0, 0, 2.5) RELATIVE detectorarm

## Slide 31
Check instrument looks okay

## Slide 32
SIMULATIONS solved a mystery on MERLIN
Views its own water moderator centrally poisoned

## Slide 33
Ei=29 meV Fermi at 600Hz
Resolution worse than it should be at detector ?

## Slide 34
Ei=29 meV Fermi at 600Hz

## Slide 35
Put new moderator in – I even signed it

## Slide 36
Ei=29 meV Fermi at 600Hz
Mystery solved -The moderator had no poisoning in it !!
Mcstas can really help finding problems

## Slide 37
Absolute flux at sample position
COMPONENT det_lmon = L_monitor(xmin=-0.005, xmax=0.005,
ymin=-0.005, ymax=0.005, nL=100, filename="det_Lmon.m", Lmin=0.0, Lmax=10)
AT (0,0,11.74) RELATIVE Origin
The way I do it!!
1) Put a wavelength monitor at the sample position with a 1cm2 area, with a 0 to 10Ǻ range with 100 bins (0.1 Ǻ bins)
2) Simulation will give counts per second per bin in monitor for a 1 µamp beam current
3) Multiply simulation output by uamp current (40 TS2 or 160 TS1) and factor of 10 to give counts/cm2.s. Ǻ

## Slide 38
Find simulation is often approx. 2 x measured
Mari spectrometer
Gem diffractometer