Capture flux and Guide losses
E. Farhi, ILL
Capture flux estimates
Definition of capture flux
Measurement and accuracy
McStas simulation
Guide losses
Mechanisms involved
Simulation
Disclaimer: in case of errors and uncertainties, please correct me...

---
Capture flux: definition
- The 'capture flux' is the standard way to measure an integrated flux in facilities. A white beam is absorbed into a gold foil, in an energy range up to 500 meV neutrons. Then this is normalized to the thermal neutron absorption cross section for l =1.8 Å (2200 m/s), and finally:
- Even though the formula is valid for thermal neutrons, it has been extended to cold and hot neutrons.
- So, in a few words, the real integrated flux
  is roughly F ~ Fc for a spectrum peaked around 1.8 Å,
  and	F ~Fc/2 for a spectrum peaked around 3.6 Å
- Capture flux = integrated, wavelength weighted flux
%PHI_c = int_0^{ 0.5eV } { { d%phi } over { d%lambda } %lambda over %lambda_{ 2200 m/s} } d%lambda
%PHI = int { { d%phi } over { d%lambda} d%lambda }

---
Capture flux: measurement accuracy
- The health physics/guide staff put 1 cm² gold foils in the beam, and they measure their activity after irradiation. Au: sabs =98.65 [barns]
- The intrinsic measurement accuracy of the method is of the order of 10 %.
- Simulating capture flux measurement with McStas:
  Monitor_nD(options= “capture per cm2”, …)
- Or use EXTEND %{ p *= 2200/v; %} before the monitor, and %{ p /= 2200/v; %} after.

---
Warning : in the following nasty neutrons will be shot
Virtual radiation hazard
Trespassers will be shot !
Survivers will be shot again !

---
Capture: Exercise 1
Aim: Capture flux after a curved guide
- Create a new Template, with input parameters Lmin=.4 and Lmax=10 for the wavelength range. Explain why Lmin = 0.4 Å (E=81.8/l²)
- Insert a Source_gen(I1=3e11, T1=330, radius=0.15/2, focus_xw=.1, focus_yh=.1, Lmin=Lmin, Lmax=Lmax) which corresponds to a 1MW thermal research reactor.
- Insert a Guide(w1=.1,h1=.1, l=1, m=2) at 2 m, with 'cheap' super-mirror coating.

---
Capture: Exercise 1
Aim: Capture flux after a curved guide
- Get Ex_3_1_curved.instr from previous session 'Guides'.
- Add a Monitor_nD(options="x lambda, all auto", xwidth=.1, yheight=.1) at 1.5 m from last Guide instance exit.
- Add a Monitor_nD(options="x lambda, all auto, capture per cm2") at 1cm from previous.

---
Capture: Exercise 1
- Save and Run in Trace mode with VRML plotter and 1000 neutrons. Check the geometry.
- Run in Simulation mode, with PGPLOT plotter and 1e6 events. Compare the ideal and capture fluxes.
- Re-run with l=0.4-5, 1-10, 2-20 Å. Compare again. How much does it vary ?

---
Guide losses: reflectivity
- Guides transporting neutrons are not 100 % efficient.
- Their reflectivity depends on the material, number and quality of the multi-layers deposited on top of the glass or metal substrate surface.
Non reflected neutrons are either absorbed or scattered. In both cases, this creates background and radiation to protect from with proper shielding (concrete, lead, boron, PE).
Divergence reflected by a guide: a[o] = 0.1 m l[Å]

---
Guide losses: origin
- Some causes of non reflection:
  - too high divergence, above total reflection angle (depends on material cross section and m-value)
  - low angle scattering
  - poor waviness of surfaces (poor polishing)
  - dirty surfaces (dust, grease, …)
- In addition to radiations, the losses damage materials by creating He (a) bubbles which propagate cracks. Glass turns dark and brittle.

---
Guide losses: Exercise 2: per m
- Re-use the previous exercise.
- Insert flux monitors in between guide elements
- Run simulation with m=0.65 (glass), 1 (Ni) and m=3 (super-mirror) for the Guide
- Estimate the losses per meter (in absolute and percentage)
- Does super mirror coating increase background level at the end of the guide ?

---
Guide losses: Exercise 3: Logger
- A set of components allow to record the 'lost' neutron events along a guide:
  - Scatter_logger/Scatter_logger_stop
  - Scatter_log_iterator/Scatter_log_iterator_stop
- Open the Test_Scatter_log_losses description from the Templates.
- Change the source 'src' into a Source_gen(I1=3e11, T1=330,...)
- Run in Simulate mode with 1e7 events.

---
Guide losses: Exercise 3: Logger
- From the description documentation, interpret the results. Determine the loss per meter (m=2).
- Does this loss correspond with that measured in Exercise 2 ?
Can you explain the difference ?