Detectors: 3He and CCD's
E. Farhi, ILL
Detectors
A bit of theory
A small Gas detector
Effect of the housing (background)
CCD scintillator
Disclaimer: in case of errors and uncertainties, please correct me...

---
Detectors: Introduction
- Simple ideal detectors are usually part of any simulation. We call them 'monitors'. Efficiency is 100%. I personally use Monitor_nD.
- Gas detectors use the absorption of n by e.g. 3He or 10B. The capture reaction creates charges which drift in a high voltage field, and are collected by wires, raising an electrical signal.
- Scintillator detectors also use capture, e.g. by 6Li, but collect photons in a PM.
- Semiconductor detectors: insert Li in Si. Work as a diode. Not considered here.

---
Detectors: 3He
- Capture: n + 3He → 3H + 1H + 765 keV;
- Helium is mixed with a stopping gas in E-field. Energy is dissipated in the 'stop' gas (CF4, CO2...). Fragments drift.
- He detectors have e.g. 70-90% detection efficiency. Low sensitivity to g. Fast (kHz).
- Cost: 10 k€/m2.
%sigma = 5333 {%lambda} over 1.8

---
Detectors: 6Li
- Capture: n + 6Li → 3H + 4He + 4.79 MeV
- Lithium is trapped in a matrix, and secondary photons are collected into a photo-multiplier.
- Scintillation efficiency for ZnS(Ag)-LiF is 9.2% and highly sensitive to g. High positional accuracy (50 µm). Slow response (Hz).
- Cost: 3 k€/400cm² (CCD, with USB)
%sigma = 940 {%lambda} over 1.8

---
Detectors: 10B
- Capture: n + 10B → 7Li + 4He + (2.3;2.8) MeV
- Boron is either as BF3 gas (toxic), or as a thin µm layer and drift gas in E-field. Fragments energy is dissipated in the gas (BF3, CF4).
- B detectors have e.g. 30-40% detection efficiency. Low sensitivity to g. Fast (kHz).
- Cost: 10 k€/m2, depends on technology.
%sigma = 3835 {%lambda} over 1.8

---
Detector efficiency
%epsilon =1-e^ { -N %sigma t}
- Efficiency:
- Where
  - s: absorption cross section
  - N: number density of absorber, 2.71019 cm-3  atm-1 in a gas
  - t: thickness in cm
- The fragments drift determines the spatial resolution.
Charges are trapped (wall effect)
Exp efficiency

---
Simple detectors in McStas
- Weight the neutron event with the exponential efficiency law.
- Done either in a dedicated component, e.g.
  - Monitor_nD(options=”3He_pressure=3”)
  - PSD_monitor_psf_eff(psf=1mm, k0=3.5, eff=0.5)
- Or in an EXTEND block
EXTEND %{ // N per cm3, T in cm, s_abs in barns
  p *= 1.0-exp(s_abs*2200/v*N/1e24*T*eff);
%}

---
Gas detectors in McStas
- The PSD_Detector component models the drift of charges in the stopping gas after capture. It also handles wall effects and parallax. Electrostatic lens correction can be added. Can generate histograms and event lists.
- All detectors can be enclosed in a 'housing' to model the effect of the Al or Fe container (produces background from Bragg and incoherent scattering).

---
Detectors: Exercise 1: gas detector
Aim: simulate a multi-wire gas detector, and estimate its resolution.
- Create a new Template instrument.
- Define an instrument input parameter(lambda=2 Å) to set the neutron wavelength.
- Insert a Source_simple(radius=0.1mm, focusing onto a 0.1x0.1 mm², with neutron wavelength=lambda and dlambda=0.1 Å).

---
Detectors: Exercise 1: gas detector
- Insert a PSD_Detector (contrib) at 2 m from PREVIOUS, with
  - size 2.6x2.6 cm², depth 2.5 cm
  - Converter="He3inHe.table" 5 bars
  - Stop gas="He3inCF4.table" 1 bar
- Save and Run. Use the Trace mode instead of Simulate.
- Click Start and look at neutron trajectories in the detector. What is happening ?
n

---
Detectors: Exercise 1: gas detector
- Re-run, in Simulate mode with 1e6 neutron events, and determine the detector intrinsic spatial resolution (given by the size of the cloud of charges) at lambda=1, 2…10 Å.
- To measure the efficiency, insert a monitor between the source and the detector, and measure the ratio=detected/incoming at lambda=1, 2…10 Å.

---
Detectors: Exercise 1: gas detector
- Add a 1 mm Al layer before the gas cell by inserting a PowderN(reflections=”Al.laz”). This is to model the detector entry window.
- Run in Trace mode and check geometry and that no volume overlap exists (use VRML or PGPLOT).
- Run the simulation again at lambda=1 to 10 Å, with PGPLOT plotter. Estimate the background from the entry window.
- Repeat the same study with reflections= ”Fe.laz” housing. Can you comment ?

---
Detectors: Exercise 1: gas detector
Now a quick correction and a few comments.

---
Detectors: Exercise 2: CCD detector
Aim: simulate a CCD/scintillator detector
- From the Neutron site menu, get the Templates/Tomography instrument.
- Click on the Edit button to show its description.
- Run in Trace with default parameters, with e.g. HTLM/VRML plotter, to check geometry.
- Run in Simulate mode, with PGPLOT plotter, sabs=5 (warning: use “quotes” around parameter opts value). Plot.

---
Detectors: Exercise 2: CCD detector
- The ZnS(Ag):LiF detector efficiency must be taken into account with N=1.18 1022 cm-3, t=1 mm, s=940 l/1.8, and a scintillation efficiency of 9.2%.
- The neutron velocity is v=√vx²+vy²+vz²
- The ratio l/1.8 is the same as 2200/v
- Derive the expression of the detector efficiency vs. neutron velocity (beware units, 1barn=10-24 cm3).
- You should get a CCD efficiency of 9.7% at l=1.8 Å.
- As a comparison, for 1 bar 3He and 1 cm thickness we get a theoretical 13.4%.

---
Detectors: Exercise 2: CCD detector
After the last component 'monitor' AT line, insert a block EXTEND %{
%}
- This block can contain any C statements.
- In the EXTEND block, multiply the neutron weight 'p' with this efficiency.
- Create afterwards a new detector similar to 'monitor' with a different name, at 1cm distance.
- Measure the efficiency, as ratio=1st/2nd monitor at lambda=1, 2…10 Å.

---
Detectors: Exercise 2: CCD detector
And the correction...