Sample Environments
E. Farhi, ILL
Sample environments
Concentric geometries
Background estimates
Separation of contributions
Disclaimer: in case of errors and uncertainties, please correct me...

---
Background ?
A sample environment is all that surrounds sample.
A background is all we do not want.
Usual environments are concentric:
- Furnaces
- Cryostats
Some may be non-concentric/symmetric:
- Magnets
- Pressure cells
- Boxes
Some materials used in sample environments:
Al, Cu, Nb, V, ...
Just a big mess that scatters everywhere...

---
Concentric geometries
- Concentric shapes in some components:
  - Incoherent
  - PowderN
  - Isotropic_Sqw
- The 'concentric=1' parameter allows to 'release' the neutron inside the shape.
- Requires to duplicate external components as if they would be formed of two half volumes.
Box, sphere, cylinder
Comp1_in = PowderN(concentric=1, ...)
  Comp2_in = PowderN(concentric=1, ...)
    Sample = Single_crystal
  Comp2_out= COPY(Comp2_in)(concentric=0)
Comp1_out = COPY(Comp1_in)(concentric=0)

---
Complex shapes
- Arbitrary polygon shapes in some components
  - Incoherent
  - PowderN
  - Isotropic_Sqw
  - Single_crystal
  - Guide_anyshape (reflecting)
- But NO simultaneous concentric support
- Used with geometry=”OFF or PLY file”
- Can be used to e.g. model housing, pillars, ...

---
SampleEnv: Exercise 1
- Re-use the Liquid_simple (9.4 Sqw) or single_crystal (9.3 SX) instruments.
- Cryostat: Add PowderN concentric shields with f 12, 9.5, 8, and 7 cm, thickness 1 mm, height 10 cm, made of “Al.laz” before the sample. Use 'concentric=1' everywhere. You may use the COPY keyword.
- Repeat in reverse order these shields after the sample with 'concentric=0'. You may use the COPY keyword.

---
SampleEnv: Exercise 1
- Run in Trace 3D mode to check the geometry.
- The incident beam is spread onto the Al shields.
- The scattering on these must be 'reduced' to 'see' the sample.
- We use p_transmit=0.95,
  p_inc=0.01
  in PowderN instances.

---
SampleEnv: Exercise 1
Re-run in Simulation/PGPLOT mode
Plot results
Interpret the results
How to separate the 'sample' contribution