Sample environments
Sample1: concentric geometries
Sample2: background estimates
E. Farhi, ILL

---
Sample environment: definition
A sample environment is all that surrounds sample.
Any material in the beam acts as a sample: it may absorb and scatter.
Usual environments are concentric:
Furnaces
Cryostats
Some may be non-concentric/symmetric
Magnets
Pressure cells
Some materials used in sample environments:
Al, Cu, Nb, ...

---
Exercise Sample1: source+sample+detector
Goal: build a simulation of a scattering sample.
Start McGUI, and click on Edit
Select menu in Editor: Insert/Instrument Template
Change instrument name as Wednesday_McStas_SampleEnv and save
Add input parameters DEFINE INSTRUMENT(lambda=2, string sample=”Na2Ca3Al2F14.laz”)
In the TRACE after Origin, insert a Source_simple(radius=0.005, dist=4,xw=0.02,yh=0.02,Lambda0=lambda,dLambda=0.1)
At 4 m, add a sample PowderN(reflections=sample, radius=0.005,yheight=0.02,d_phi=50)
Around the sample, add a banana detector Monitor_nD(radius=2,yheight=1, options="banana theta y, auto", bins=180)
Run simulation. Observe onion rings (scattering from a powder gives rings which angle give the atomic spacing). Press 'L' key for log-scale

---
Simulating a concentric arrangement
With McStas, any concentric geometry should be described symmetrically w.r.t. the sample position, e.g. :
COMPONENT entry_side= Comp(blah, concentric=1)
COMPONENT sample= …
COMPONENT exit_side= COPY(entry_side)(concentric=0)
This works for the powder and liquid/amorphous/glassy materials.

---
Simulating a concentric arrangement
Goal: surround the previous sample with a cylinder of Aluminium
Before the Sample, add a cylinder entry_side=PowderN(reflections=”Al.laz”, radius=0.035, radius_i=0.035-0.0002,d_phi=50,tfrac=0.8,concentric=1) centred on the sample
After the sample, add a exit_side=COPY(entry_side)(concentric=0)
Re-run simulation. Are there additional rings ?
In the DECLARE %{ … %} add int flag_env,flag_sample;
EXTEND the Origin with flag_env=flag_sample=0;
EXTEND PowderN components with e.g. if (SCATTERED) flag_blah=1; where blah is 'sample' or 'env'
Duplicate the Detector with copies that only activates WHEN (flag_blah)
Re-run. Compare the intensity from the sample and the environment.

---
What you should get
Trace 3D view (Matlab or VRML)
Simulate