intro
An introduction to
Neutron Scattering
Virtual Experiments
E. Farhi, ILL

---
MC:why
Why simulate neutron instruments+samples ?
Design new instruments
Optimize existing instruments (flux/resolution)
Optimize usage of existing instruments (better experiments)
Get accustomed with the instruments before actually using them
Measure the instrument effects on the simulated 'ideal' sample signal
Estimate complex effects like :
absorption, multiple scattering, geometry, resolution function...
Compare virtual experiments with real ones, possibly during exp.

---
VirtInstr
Virtual experiments
Virtual experiments
=
Instrument simulation
⊗
Realistic Sample model
=
Neutron flight simulator
and then we play with it without breaking the instrument and sample

---
A bit of theory for neutron-sample interaction
See Egelstaff or H. Fischer, Rev. Prog. Phys. 69 (2006) 233
Neutronist's Mantra
Holy Book (Squires)
Effective cross section
for scattered intensity
 V.F. Sears. Adv. Phys., 24, 1, 1975.
We like to play games
in (q,w) space
Effective cross section
in (q,w) space
p=func e^{-%rho hat %sigma x}
Probability to interact
with importance sampling to
scatter preferably where S is large
Scattering distribution
S(q,w)

---
Liquid Indium real and virtual experiment
Liquid Indium:
Very low scattering cross section (good luck)
Very high absorption (good luck)
Never measured with neutrons (good luck)
Proposal includes both real and virtual experiment:
Simulation showed we would be able to measure the quasi-elastic line
Around the first structure peak in S(q).
Experiment:
Levitation furnace (gas flow+laser)
T=450 K
IN22 Ei=30.8 meV
Team: E. Farhi, P. Willendrup, L.P.Regnault, McStas <mcstas.org>
Plotting with <ifit.mccode.org>

---
Liquid Indium real experiment
Data includes contribution from the furnace and the B4C nozzle.
Sample is a f=4mm diameter sphere
Experiment produces...
?
Background ?
Structure peak position

---
Liquid Indium: Ab-Initio Molecular Dynamics
We use VASP
200 atoms in a 17 Å cube
Record atoms dynamics for 36 ps
Compute S(q,) using nMoldyn
Coherent part
Incoherent part
We show here the measurement range
Compared to experiment,
computed S(q,) is very clean

---
Liquid Indium: Virtual experiment
We use McStas <mcstas.org> to model the reactor, the H25 supermirror
Guide and the IN22 triple-axis spectrometer.
Model includes levitation furnace and nozzle.
We run on 80 cores for 4 hours to
simulate all q-energy scans.

---
Liquid Indium: Virtual experiment DONE
Total signal shows
a tail after the
structure peak
Coherent part
Incoherent part
Furnace contribution
Virtual experiment enables to
prepare and understand
the measurement.
l-In measured with neutron

---
Similar study with l-Rb data from Copley
Virtual experiments: Combining realistic neutron scattering instrument and sample simulations
E. Farhi, V. Hugouvieux, M.R. Johnson, W. Kob, Journal of Computational Physics 228 (2009) 5251–5261