## Slide 1: McStas advanced language features - and other important, not so well known details
Peter Willendrup1,5
Emmanuel Farhi2
Erik Knudsen1,5
Uwe Filges3
Kim Lefmann4,5
1DTU Physics, Lyngby, Denmark
2Calcul Scientifique, Institut Laue-Langevin (ILL), Grenoble, France
3Niels Bohr Institute, University of Copenhagen, Copenhagen, Denmark
4Paul Scherrer Institut, Villigen, Switzerland
5ESS DMSC, Copenhagen, Denmark

## Slide 2: Topics
A quick recap of the most important vocabulary
Simulation to experiment comparison
How to make your McStas more efficient
McStas language macros
Other important details

## Slide 3: McStas: key concepts
Time (t)

## Slide 4: McStas: key concepts
Time (t)
Neutron state parameters are global variables!

## Slide 5: McStas: key concepts

## Slide 6: McStas: key concepts

## Slide 7: McStas: key concepts
Local, internal coordinate system!

## Slide 8: McStas: key concepts

## Slide 9: Under-the-hood / inner workings
Domain-specific-language (DSL) based on compiler technology (LeX+Yacc)
    Simple Instrument language ISO C
Component codes realizing beamline parts (including user contribs)
Library of common functions for e.g.
    I/O
    Random numbers
    Physical constants
    Propagation
    Precession in fields
    ...
Code generation

## Slide 10: From the “list of frequent questions”
Why do you need to have the components in this order?

## Slide 11: Order of components is important
1
1
2
2
3
3
Starting at the source

## Slide 12: Order of components is important
1
1
2
2
3
3
Moving to first comp in the list

## Slide 13: Order of components is important
1
1
2
2
3
3
Moving to 3rd comp in list requires “moving back in time”.
Default behavior is to ABSORB this type of neutron.
For monitors use restore_neutron=1 in this case.
For homegrown comps use ALLOW_BACKPROP macro.

## Slide 14: Further tips 1:
Simulation to experiment comparison

## Slide 15: What is really the information content…?
McStas sources generally provide “intensity” in units of neutrons/s (into a chosen solid angle)
That intensity is carried through the instrument on a discrete set of “neutron rays”

## Slide 16: In a histogram sense
Imagine a histogram, e.g. I(λ)
The RMS variance over that set becomes our statistical error bar E
…
…
In bin i, N events each carrying a fractional intensity pj so that
1
2
i
k
3

## Slide 17: In a histogram sense
Imagine a histogram, e.g. I(λ)
The RMS variance over that set becomes our statistical error bar E
…
…
1
2
i
k
3
In bin i, N events each carrying a fractional intensity pj so that
I
E
N

## Slide 18: From "Virtual experiments - the ultimate aim of neutron ray-tracing simulations", K. Lefmann et al., Journal of Neutron Research 16, 97-111 (2008)

## Slide 19: From "Virtual experiments - the ultimate aim of neutron ray-tracing simulations", K. Lefmann et al., Journal of Neutron Research 16, 97-111 (2008)

## Slide 20: Sketch of an algorithm…
On a given McStas histogram
For the non-zero bins, calculate
The smallest defines the “maximal counting time” allowed by your statistics
Preferably a “background” should be added - use a “known experimental value” or an estimate…

## Slide 21: Important points to remember
Your simulation will only contain elements you provided / defined
… to the precision you defined
Answers the questions you posed
Background essentially only from “sample”, or sample-near objects

## Slide 22: Further tips 2:
How to make your McStas more efficient

## Slide 23: Onto efficiency…
Apply focusing techniques
  At the source (spatially, temporally, in wavelength…)
  At the sample, if possible
(carefully!) Apply SPLIT - but only if immediately followed by Monte Carlo choices, e.g. in sample
Alternatively use MCPL o/i which allows repetition - beware of biases!

## Slide 24: Onto efficiency…
Apply focusing techniques
  At the source (spatially, temporally, in wavelength…)
  At the sample, if possible
(carefully!) Apply SPLIT - but only if immediately followed by Monte Carlo choices, e.g. in sample
Alternatively use MCPL o/i which allows repetition - beware of biases!
All of this can be considered “variance reduction”
or biasing

## Slide 25: Onto efficiency…
Use MPI parallelisation - included in macOS install from 2.4, easy to get on Linux…
The Intel C compiler is known to give ~factor of 2 wrt. gcc in most cases
- Still consider if you are asking the right question if runtimes reach days/weeks…

## Slide 26: Onto efficiency…
Use MPI parallelisation - included in macOS install from 2.4, easy to get on Linux… (Windows: see later slide)
The Intel C compiler is known to give ~factor of 2 wrt. gcc in most cases
- Still consider if you are asking the right question if runtimes reach days/weeks…
Sledge-hammer / brute force!

## Slide 27: Advanced language features
Macros and tricks for your instrument...

## Slide 28: DECLARE / INITIALIZE
Use the DECLARE section define user variables and functions.
    DECLARE %{
    double myvar;
    %}
Use INITIALIZE for initialization of user variables and calculations.
    INITIALIZE %{
    myvar = sqrt(PI*input_var)*rand01();
    %}
- Both use normal c-syntax.
BEWARE: (example) What you do in the c-style areas is c-standard, e.g. trigonometric functions from math.h use radians! - McStas placement specifiers work in degrees, etc...
K & R

## Slide 29: %include
Instrumentfiles can include external c-code or other instrumentfiles... See the examples:
ILL_H15_IN6.instr:%include "monitor_nd-lib"
ILL_H16_IN5.instr:%include "ILL_H16.instr"
ILL_H25_IN22.instr:%include "ILL_H25.instr"
ILL_H25_IN22.instr:%include "templateTAS.instr"
Used in the DECLARE section

## Slide 30: Syntax in one, complex view...
{SPLIT} COMPONENT name = comp(parameters) {WHEN condition}
AT (...) [RELATIVE [reference|PREVIOUS] | ABSOLUTE]
{ROTATED {RELATIVE [reference|PREVIOUS] | ABSOLUTE} }
{GROUP group_name}
{EXTEND C_code}
{JUMP [reference|PREVIOUS|MYSELF|NEXT] [ITERATE number_of_times | WHEN condition] }

## Slide 31: SPLIT
Increase statistics beyond this point in the instrumentfile
SPLIT n MyArm = Arm()
AT somewhere
will “formulate an if-statement”:
for j=1:n
comp1
comp2
comp3
...
end (of instrument)
ONLY meaningful in case of Monte Carlo choices after SPLIT point...

## Slide 32: SPLIT
Increase statistics beyond this point in the instrumentfile
SPLIT n MyArm = Arm()
AT somewhere
will “formulate an if-statement”:
for j=1:n
comp1
comp2
comp3
...
end (of instrument)
ONLY meaningful in case of Monte Carlo choices after SPLIT point...

## Slide 33: Problem: McStas Single_crystal.comp “slow” for large unit cell diffraction studies
Example: Rubredoxin
  Reflection list ~ 124 K reflections (still “small” in the PX world!!)
slight sidetrack….

## Slide 34: Algorithm improvement: Use incoming neutrons more efficiently - scatter each one on all possible reflections
Red: Original algorithm, one incoming neutron used only once
Blue: Improved algorithm, each incoming neutron scattered (via SPLIT keyword) all possible times
Component makes estimate on average number of “active” diffraction spots - in the case Rubredoxin this is around 50!
slight sidetrack….

## Slide 35: Sim data speak for themselves - 1e9 rays
Old comp
New comp
Rubedoxin
124K reflections
Predeuterated pyrophosphatase
1.7M reflections
~ Factor 50
more efficient
~ Factor 500
more efficient
slight sidetrack….

## Slide 36: WHEN
Syntax:
COMPONENT Mine = Yours(blah, blah)
WHEN (c-expression) AT (....)
Is very powerful when combined with EXTEND and user variables, or as a method to let input parameters select if certain components are active.
Example: Use EXTEND to flag if neutron was scattered on one monochromator blade or another. Then later use WHEN to only show contribution from blade N at sample position?
COMPONENT Mon = PSD_monitor(...)
WHEN (myvar==1) AT (0,0,0) RELATIVE Sample
K & R

## Slide 37: GROUP - components working in parallel
  COMPONENT Mono1 = Monochromator_curved(...)
  AT (0,0, -LMM) RELATIVE Cradle ROTATED (0,A1/2,0) RELATIVE Cradle
  GROUP IN6Monoks
  COMPONENT Mono2 = Monochromator_curved(...)
  AT (0,0, 0) RELATIVE Cradle ROTATED (0,A2/2,0) RELATIVE Cradle
  GROUP IN6Monoks
  - One comp after the other is “tried” in sequential order until the neutron was SCATTERED.

## Slide 38: EXTEND
Enrich component behaviour using EXTEND:
COMPONENT Mono1 = Monochromator_curved(...)
AT (0,0, -LMM) RELATIVE Cradle ROTATED (0,A1/2,0) RELATIVE Cradle
GROUP IN6Monoks
EXTEND
%{
if (SCATTERED) { myvar = ;1 }
%}
...
COMPONENT Mono2 = Monochromator_curved(...)
AT (0,0, 0) RELATIVE Cradle ROTATED (0,A2/2,0) RELATIVE Cradle
GROUP IN6Monoks
%{
if (SCATTERED) { myvar = 2 }
%}
K & R

## Slide 39: JUMP
A goto. Be careful. Can be used in two situations:
JUMP to myself
JUMP to an Arm
No coordinate transformations are applied... (Meaning that if the Arms you JUMP between do not coincide you will “move” / “reorient” the neutrons...)
Syntaxes:
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP somewhere
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP somewhere
Van Halen...

## Slide 40: JUMP
A goto. Be careful. Can be used in two situations:
JUMP to myself
JUMP to an Arm
No coordinate transformations are applied... (Meaning that if the Arms you JUMP between do not coincide you will “move” / “reorient” the neutrons...)
Syntaxes:
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP somewhere
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP somewhere
Van Halen...
BEWARE - This IS a GOTO!

## Slide 41: JUMP
A goto. Be careful. Can be used in two situations:
JUMP to myself
JUMP to an Arm
No coordinate transformations are applied... (Meaning that if the Arms you JUMP between do not coincide you will “move” / “reorient” the neutrons...)
Syntaxes:
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP somewhere
COMPONENT a=b(...)
WHEN (expr) AT (...) JUMP somewhere
Van Halen...
BEWARE - This IS a GOTO!

## Slide 42: COPY- inside instruments
In instruments: (see ILL_H25.instr)
COMPONENT H25_1 = Guide_gravity(
w1=0.03, h1=0.2, w2=0.03, h2=0.2, l=L_H25_1,
R0=gR0, Qc=gQc, alpha=gAlpha, m=m, W=gW)
AT (0,0,Al_Thickness+gGap) RELATIVE PREVIOUS
ROTATED (0,Rh_H25_1,0) RELATIVE PREVIOUS
COMPONENT COPY(H25_1) = COPY(H25_1)
AT (0,0,L_H25_1+gGap) RELATIVE PREVIOUS
ROTATED (0,Rh_H25_1,0) RELATIVE PREVIOUS
COMPONENT COPY(H25_1) = COPY(H25_1)(W=2*gW)
AT (0,0,L_H25_1+gGap) RELATIVE PREVIOUS
ROTATED (0,Rh_H25_1,0) RELATIVE PREVIOUS

## Slide 43: Other advanced topics
Tricks, macros and functions for your components

## Slide 44: COPY In components:
+
+
=

## Slide 45: MPI on Windows
Get both of the installers from
  https://github.com/McStasMcXtrace/McCode/tree/master/support/Win32/MSMPI
  - install them
Dump this batchfile in bin dir of your McStas installation:
  https://github.com/McStasMcXtrace/McCode/blob/master/cmake/support/run-scripts/mpicc.bat
Add C:\Program Files\Microsoft MPI\Bin\ to your system PATH

## Slide 46: NeXus libs on Windows
Get last release from
  https://github.com/nexusformat/code/releases?after=4.3.1
  Install it
Use the MCSTAS_CFLAGS_OVERRIDE or the GUI File->Configuration entry to specify -I and -L directives for linking
i.e.
-DUSE_NEXUS -lNeXus-0
-L"C:\Program Files (x86)\NeXus Data Format\bin" -L"C:\Program Files (x86)\NeXus Data Format\lib\nexus" -I"C:\Program Files (x86)\NeXus Data Format\include"

## Slide 47: NeXus libs on macOS
Get homebrew via https://brew.sh
Install it via the recipe given
In a terminal, issue
Use these CFLAGS either via env var or gui
DTUs-MacBook-Pro:Downloads dtuphysics$ brew search nexusformat
homebrew/science/nexusformat ✔
DTUs-MacBook-Pro:Downloads dtuphysics$ brew install homebrew/science/nexusformat
-DUSE_NEXUS -lNeXus -L/usr/local/lib -I/usr/local/include

## Slide 48: The end