## Slide 1
ESS DMSC McStas training
Oct 31st-Nov 2nd 2018
McStas Introduction

## Slide 2: Agenda
A (very) brief introduction to neutrons, Monte Carlo & raytracing
Components of neutron instruments
How McStas works under the hood
Components and instruments
A demo

## Slide 3: McStas: Neutrons, Monte Carlo & ray-tracing
Subatomic particle discovered by
Sir James Chadwick, 1932

## Slide 4: The Neutron
,
Mr. Neutron

## Slide 5: Nobel Prize in Physics, 1994
Awarded for “pioneering contributions to the development
of neutron scattering techniques for studies of condensed matter”
Neutron spectroscopy
Neutron diffraction technique
Bertram N. Brockhouse Clifford G. Shull

## Slide 6: 1994 Nobel prize to Shull & Brockhouse

## Slide 7: Neutron facilities

## Slide 8: Origin of Monte Carlo methods
Used by Nature since ... (a long time) : diversity of Life
First application using computers:
Metropolis, Ulam and Von Neumann at Los Alamos, 1943
Neutron Scattering and Absorption in U and Pu, Origin of MCNP
Name:
Monte Carlo casino, a random generator (Ulam’s father played poker)

## Slide 9: What are Monte Carlo methods ?
Use random generators (play poker)
Explore a complex and large phase space (many parameters)
Integrates microscopic random events into measurable quantities not a usual regular sampling integration
Metropolis algorithm: model energy gap E as a probability
Integrals converge faster than any other method (for d > 3) when using enough independent events (central limit theorem)
F. James, Rep. Prog. Phys., Vol. 43 (1980) 1145.

## Slide 10: How to implement Monte Carlo methods ?
or quasi-random generators => quasi-Monte-Carlo
We encounter a probability 0 < p < 1.
Crude Monte-Carlo (yes/no choice):
We shoot n events x Î[0,1]
We keep events that satisfy x < p
np events → low statistics
Importance sampling (fuzzy choice – event weighting):
Keep n events, no more random number...
But associate a weight p to each of them (we set x = p)
Retain statistical accuracy (1/÷n)
Good random generator:
from thermal electronic noise (hardware)

## Slide 11: When to use Monte Carlo methods
Dimensionality of phase space must be large (d > 5)
Overall complexity is beyond reasonable analytical methods
p
Number of points for which
{ x2+y2£ 1, (x,y) Î [0,1] }
Ratio circle/square → p/4
Each event can be computed easily and independently MC is the 'lazy guy' method – think microscopic
Examples:
Estimate p from a circle/square (“Buffon needle”)
Area under/inside a curve/volume (integration)
Molecular Dynamics
spin-system phase transitions (Ising model)
nuclear reactions
ray-tracing (light, particles)

## Slide 12: Examples of Monte Carlo programs
Each time physics takes place (scattering, absorption, …)
random choices are made.
Light ray-tracing: PoV-RAY and others ...
Nuclear reactor simulations (neutron transport):
MCNP, Tripoli, GEANT4, FLUKA
Neutron Ray-Tracing propagation:
McStas <www.mcstas.org>, Vitess, Restrax, NISP, IDEAS
Neutrons are described as (r, v, s, t), and are transported along
instrument models.
Propagation simply uses Newton rules, incl. gravitation.
X-ray tracing
Shadow, McXtrace, RAY, …

## Slide 13: Monte Carlo techniques
Los Alamos has since then developed and perfected many different monte carlo codes leading to what is today known as the codes MCNP5 and MCNPX
State of the art is MCNPX (or soon the merged MCNP6 code) that features numerous (even exotic) particles
MCNP was originally Monte Carlo Neutron Photon, later N-Particle
Mainly used for high-energy particle descriptions in weapons, power reactors and routinely used for estimating dose rates and needed shielding
Does not to date handle coherent scattering of neutrons due to the focus on high energies

## Slide 14: Ray-tracing methods
When neutrons move in “free space”, we use ray-tracing - but in most cases in direction source -> detector
Of course parabolas rather than straight lines are uses to implement gravity

## Slide 15: Elements of Monte-Carlo raytracing
Instrument Monte Carlo methods implement coherent scattering effects
Uses deterministic propagation where this can be done
Uses Monte Carlo sampling of “complicated” distributions and stochastic processes and multiple outcomes with known probabilities are involved
- I.e. inside scattering matter
Uses the particle-wave duality of the neutron to switch back and forward between deterministic ray tracing and Monte Carlo approach
Result: A realistic and efficient transport of neutrons in the thermal and cold range

## Slide 16: Components of neutron instruments

## Slide 17: Moderators... (Where McStas starts)

## Slide 18: Neutron guides

## Slide 19: Collimators & slits

## Slide 20: Disk Choppers

## Slide 21: Velocity selector

## Slide 22: Fermi Choppers

## Slide 23: Crystal monochromators (and analyzers)

## Slide 24: Samples studied...

## Slide 25: Detectors
x

## Slide 26: McStas Introduction
Flexible, general simulation utility for neutron scattering experiments.
Original design for Monte carlo Simulation of triple axis spectrometers
Developed at DTU Physics, ILL, PSI, Uni CPH, ESS DMSC
V. 1.0 by K Nielsen & K Lefmann (1998) RISØ
Currently 2.5+1 people full time plus students
GNU GPL license
Open Source
mcstas-users@mcstas.org mailinglist
Project website at
http://www.mcstas.org

## Slide 27: McStas Introduction
Flexible, general simulation utility for neutron scattering experiments.
Original design for Monte carlo Simulation of triple axis spectrometers
Developed at RISØ DTU, KU and ILL, Grenoble.
V. 1.0 by K Nielsen & K Lefmann (1998)
Currently 2.5+1 people full time plus students
4
GNU GPL license
Open Source
neutron-mc@risoe.dk mailinglist
Project website at
http://www.mcstas.org
McXtrace - since jan 2009 similar for X-rays
Synergy, knowledge transfer, shared infrastructure

## Slide 28: Used in many places

## Slide 29: What is McStas used for?
Instrumentation
Planning
Construction
Virtual experiments
Data analysis
Teaching
(KU, DTU)

## Slide 30: Instrumentation
Design and optimization of instruments

## Slide 31: Virtual experiments (VE) (definition:)
P. Willendrup, Risø DTU; Uwe Filges, L. Keller, PSI
A. Daud-Aladine, ISIS
Simulation of a complete experiment
… from source to detector
Ideally controlled like real experiment.
Data analysed by ”real” analysis programs

## Slide 32: Data analysis (1) (using VE techiques)
E. Farhi, ILL
Virtual TOF exp. at IN6, ILL
Liquid Ge sample
Coherent / incoherent
Multiple scattering
And sample environment
All contributions can be separated by VE !

## Slide 33: Data Analysis (2) (using VE techniques)
VE data has been used to test data analysis programs
… and to check resolution effects
P. Tregenna-Piggott, PSI
L. Udby, Risø-DTU

## Slide 34: Teaching / training purposes
Workshops
Teaching
    University of Copenhagen course on Neutron Scattering 2005-, DTU 2011-

## Slide 35: Reliability - cross comparisons
Much effort has gone into this
Here: simulations vs. exp. at powder diffract. DMC, PSI
The bottom line is
McStas agree very well with other packages (NISP, Vitess, IDEAS, RESTRAX, ...)
Experimental line shapes are within 5%
Absolute intensities are within 10%
Common understanding: McStas and similar codes are reliable
P. Willendrup et al., Physica B, 386, (2006), 1032.
E. Farhi, P. Willendrup et al., in preparation

## Slide 36: McStas: key concepts
Time (t)

## Slide 37: McStas: key concepts

## Slide 38: McStas: key concepts

## Slide 39: McStas: key concepts
Local, internal coordinate system!

## Slide 40: McStas: key concepts

## Slide 41: In the big picture…

## Slide 42: McStas overview
Portable code (Unix/Linux/Mac/Windoze)
Ran on everything from iPhone to 1000+ node cluster!
'Component' files (~100) inserted from library
    Sources
    Optics
    Samples
    Monitors
    If needed, write your own comps
DSL + ISO-C code gen.

## Slide 43: Under-the-hood / inner workings
Domain-specific-language (DSL) based on compiler technology (LeX+Yacc)
    Simple Instrument language ISO C
Component codes realizing beamline parts (including user contribs)
Library of common functions for e.g.
    I/O
    Random numbers
    Physical constants
    Propagation
    Precession in fields
    ...
Code generation

## Slide 44: Implementation

## Slide 45: Instrument file

## Slide 46: Component file

## Slide 47: Generated c-code

## Slide 48: Writing new comps or understanding existing is not that complex...
Check our long list of components and look inside... Most of them are quite simple and short... Statistics:
(update: 175)
Number of lines of code per component - 199 comps in total

## Slide 49: Including user contribs
Well-developed community support
  30-40% of existing and new additions are from users
  No direct refereeing of the code, but these requirements:
      At least one test-instrument
      Meaningful documentation headers (in-code docs)
  Contributions go in dedicated contrib/ section of library
Natural life-cycle of contrib’s
  Bug-fixes are applied both by contributor and developers
  If contributor becomes unavailable either:
      Many users of comp: Promote to official components, e.g. in optics/
      Few/no users of comp: Move to obsolete/ until next major release

## Slide 50: Example suite: ~140 instruments