## Slide 2: Exercise: McStas-Mantid
Purpose of the exercise is to be familiar with some McStas–Mantid key words
Learn how to use McStas-Mantid interface
Learn about the Nexus file format
Learn about IDF (Mantid Instrument Definition file)
Learn how-to use already developed (reduction) algorithms in Mantid
Learn about Python scripting in Mantid
McStas files:
  templateSANS.instr
  templatedSANS_Mantid.instr
  templatedSasview_Mantid.instr

## Slide 3: McStas-Mantid workflow
The McStas Nexus file must contain:
Event data, i.e each neutron has a pixel id and a time stamp
An IDF
McStas monitor_nD gives pixle id & time for each event
mcdisplay can auto-generate an IDF
Nexus file
Mantid

## Slide 4: NeXus fileformat
A number of large-scale neutron facilities use the NeXus data format for storing neutron data.
NeXus is derived from the Hierarchical Data Format (HDF)
Mantid uses the Nexus file format
McStas can out put Nexus file format

## Slide 5: Neutron information
Information only available on detector planes
# 2 paramtes | # 11 parameters
pixel id | 
time | 
 | t: time
 | r: coordinates x,y,z
 | v: velocity vx,vy,vz
 | s: spin sx, sy,sz
 | p: neutron weight
Mantid

## Slide 6: Mantid: IDF & TOF
Mantid was designed for data reduction at TOF spallation neutron sources
Mantid’s IDF store geometry information use in TOF analysis
This implies parsing information about:
  where the neutron source is located,
  where the sample is located,
  where each individual detector pixel is located.

## Slide 7: McStas – Mantid: Rules I
How-to generate McStas event data for Mantid
Step 1. Compile McStas instrument code:
mcstas templateSANS_Mantid.instr –trace
Step 2. Compile c code:
gcc -o templateSANS_Mantid.out templateSANS_Mantid.c -lm -DUSE_NEXUS -lNeXus
Step 3. Generate IDF:
mcdisplay templateSANS_Mantid.instr --format=Mantid -n0
Step 4. Run simulation:
./templateSANS_Mantid.out --format=Nexus

## Slide 8: McStas – Mantid: Rules II
McStas event data conventions
McStas instrument file name and the McStas defined name of the instrument must be the same:
E.g. templateSANS_Mantid.instr and “DEFINE INSTRUMENT templateSANS_Mantid(…. )”
In the McStas instrument file the source must be named “sourceMantid”
E.g. "COMPONENT sourceMantid = Source_simple(…. )"
In the McStas instrument file the sample must be named “sampleMantid”
E.g. "COMPONENT sampleMantid = Sans_spheres(…. )"
In the McStas instrument file the event monitors must be named “nD_Mantid_#”
E.g. "COMPONENT nD_Mantid_1 = Monitor_nD(…. )"

## Slide 9: Exercise I: McStas-Mantid
Load templateSANS.instr
Run simulation in mcgui (only ascii – no Nexus yet)
Plot data
Load templateSANS_Mantid.instr
Run simulation in mcgui (only ascii – no Nexus yet)
Plot data
Compare results
  Whys does scattering pattern (and intensity) differ on the two versions?

## Slide 10: Exercise II: McStas-Mantid
Use templateSANS_Mantid.instr to make a Nexus file for Mantid
Compile McStas code (See Rules I)
Make IDF file
Run simulation
Start Mantid
  Load data into Mantid
  Play with Mantid interface

## Slide 11: Exercise III: McStas-Mantid
Use templateSANS_SasView.instr to make a nexus file for Mantid
Compile McStas code (See Rules I)
Make IDF file
Run simulation
Start Mantid
  Load data into Mantid
  Reduce event data in Mantid as described in the templateSANS_SasView.instr file

## Slide 12: Exercise IV: McStas-Mantid
Load ISIS_SANS2D.instr
Edit *.instr file and make it ready for Mantid
Use the Rules I & II
Compile McStas code
Make IDF file
Run simulation
Start Mantid
  Load data into Mantid
  Reduce data in Mantid
  Does data fit?

## Slide 13: Exercise V: McStas-Mantid
Write a python script in Mantid which will load and reduce the data
Use data from templateSasView_Mantid.instr
See link below about Mantid and Python
TIP: one can save the “history” of used algorithms operations on an data set into a python file

## Slide 14: Exercise VI: McStas-Mantid
Write your own IDF file for templateSANS_Mantid.instr
Look at the Mantid link on howto generate an IDF (See link below)
Or search for IDF in Mantid search tool

## Slide 15: Exercise VII: McStas-Mantid
Download HDF view or nexpy (python package) to look inside a HDF file
Open mccode.h5 from the templateSANS_Mantid.instr file and search for the IDF data
Browse through the meta data in the file

## Slide 16: Exercise VIII: McStas-Mantid
Load templateSANS_Mantid.instr
Make one simulation with Nexus output data for Mantid
Remove the “Beam Stop” in the templateSANS_Mantid.instr file
Make a second simulation with Nexus output data for Mantid
Remove the “Sample” in the templateSANS_Mantid.instr file
Make a thrid simulation with Nexus output data for Mantid
Use the same “seed” for all simulations, eg. –seed=117
Compare the three simulations in Mantid. When should they be equal?

## Slide 17: Summary
You should have learned how to use McStas and Mantid
With a little training be convinced that many of Mantid algorithms can easily be used for virtual experiments (McStas simulations)

## Slide 18: Links
McStas:
https://github.com/McStasMcXtrace/McCode/wiki/McStas-and-Mantid
IDF:
http://docs.mantidproject.org/nightly/concepts/InstrumentDefinitionFile.html
NeXus:
http://www.nexusformat.org
HDF view:
https://www.hdfgroup.org/HDF5/
Mantid and Python:
http://www.mantidproject.org/Python_In_Mantid