An introduction to neutron scattering with McStas
E. Farhi, ILL/Computing for Science
Staff: 400
Exp./y: 1100+
~30 instruments

---
The Neutron
- Non charged particle
- Mass ~ 1.675 10-27 kg
- E[meV] = 81.81 / l2[Angs] and l = 2p/k
- v[m/s] = 629.62 k[1/Angs]
- 1 meV ~ 11.604 K ~ 8.06 cm-1 ~ 241.8 GHz
- Cross section: coh+inc+abs

---
~~~ The Menu ~~~
- What is Monte-Carlo ? (not only a casino)
- Instrument simulation codes
- Instrument components
- Examples of neutron instruments
- Virtual experiments
- What we can do with TRIGA@PUSPATI
- Exercises

---
MCorigin
Origin of Monte Carlo methods
Used by Nature since ... (a long time) : diversity of Life
First application using computers:
Metropolis, Ulam and Von Neumann at Los Alamos, 1943
Neutron Scattering and Absorption in U and Pu, Origin of MCNP
Name:
Monte Carlo casino, a random generator (Ulam played poker)
Photograph Source: GALE FORCE Archive

---
MCwahtis
What are Monte Carlo methods ?
Use random generators (play poker)
Explore a complex and large phase space (many parameters)
Integrates microscopic random events into measurable quantities
not a usual regular sampling integration
Metropolis algorithm: model energy gap E as a probability
p a e-E/kT
Integrals converge faster than any other method (for d > 3)
when using enough independent events (central limit theorem)
lim from{n%tendto%infinite} {{1} over {n}} sum from{i=1,a<u_i<b} to{n} f(u_i) = {{1} over {b-a}} int from{a} to{b} f(u) du
F. James, Rep. Prog. Phys., Vol. 43 (1980) 1145.

---
MChow
How to implement Monte Carlo methods ?
Good random generator:
from thermal electronic noise (hardware)
or quasi-random generators => quasi-Monte-Carlo
We encounter a probability 0 < p < 1.
Crude Monte-Carlo (yes/no choice):
We shoot n events x [0,1]
We keep events that satisfy x < p
np events → low statistics
Importance sampling (fuzzy choice – event weighting):
Keep n events, no more random number...
But associate a weight p to each of them (we set x = p)
Retain statistical accuracy (1/√n)

---
MCwhen
When to use Monte Carlo methods
Dimensionality of phase space must be large (d > 5)
Overall complexity is beyond reasonable analytical methods
Each event can be computed easily and independently
MC is the 'lazy guy' method – think microscopic
Examples:
Estimate p from a circle/square (“Buffon needle”)
Area under/inside a curve/volume (integration)
Molecular Dynamics
spin-system phase transitions (Ising model)
nuclear reactions
ray-tracing (light, particles)
p
Number of points for which
{ x2+y2  1, (x,y)  [0,1] }
Ratio circle/square → p/4

---
MCprograms
Some Monte Carlo programs
Each time physics takes place (scattering, absorption, ...) random choices are made.
Light ray-tracing: PoV-RAY and others ...
Nuclear reactor simulations (neutron transport):
MCNP, Tripoli, GEANT4, FLUKA
Neutron Ray-Tracing propagation:
McStas <www.mcstas.org>, Vitess, Restrax, NISP, IDEAS
Neutrons are described as (r, v, s, t), and are transported along models.	Propagation simply uses Newton rules, incl. gravitation.
X-ray tracing
Shadow, McXtrace

---
Presentation of McStas

---
McStas: History, funding, team
Flexible, general simulation utility for neutron scattering experiments.
Original design for Monte Carlo Simulation of triple axis spectrometers.
Developed at RISØ and ILL (started 1998) by K. Lefmann and K. Nielsen.
Mainly funded by EU (FP 4-7): P. Willendrup, E. Farhi, E. Knudsen/2 + others
Open source, GPL2. Works on all systems (Linux, Win$, MacOSX, iPhone...)
Most widely used code in its ecological niche (compared to other similar codes)..
A few hundred users worldwide (230 registered)
some contributors (community based).
Has been used to model most existing and future
neutron scattering instruments.
mcstas-users@mcstas.org mailing list
mcstas-support@mcstas.org developer contact
<www.mcstas.org>

---
Main capabilities of McStas
McStas requires an instrument description (text)
Many instrument examples are given with
the software, covering all instrument
classes (TOF, TAS, SANS, DIF, ...).
Parameters
3D view
EXE
Results
'Monitors'
McStas creates an instrument executable
model for which configuration parameters can be changed at will.

---
The McStas guts (it works but you don't feel it)
Components
n=(r,v,t,s)
n'
Kernel
Propagation between components
Positioning, geometry, random numbers...
Code generation (in C) from meta language
Component level
Physics
Interactions neutron ↔ Matter
Instrument
Relative positions of components
Interaction with you
Can be executed as single shot, scans, geometry view and optimize mode
Instrument

---
What you get when using McStas
Main instrument components
Sources (area, Maxwellian, events from other MC codes, pulsed)
Optics (slits, monochromators, moving optics, guides...)
Samples (powders, colloids, Xtals, liquids and amorphous). Most of the physics is here (structure, dynamics)
Detectors/Monitors (write data files in many formats).
Main instrument examples:
We have example instruments for all type of experiments
Virtual experiments
Tools:
3D view of instruments and particle trajectories
Instrument editor (text file)
Data plotter
Cluster support (MPI, grid) up to 1000 cpu
Optimizers (embedded and with <Fit.mccode.org>

---
Simulating instrument: what for ?
A Triple-Axis
Spectrometer (IN20)
n
M
M
A
A
S
S
Design new instruments
Optimize existing instruments (flux/resolution)
Optimize usage of existing instruments (better experiments)
Get accustomed with the instruments before coming at the ILL
Measure the instrument effects on the simulated 'ideal' sample signal
Estimate complex effects like :
absorption, multiple scattering, geometry, resolution function...
Compare virtual experiments with real ones, possibly during exp.

---
What Mcstas does
- Propagates neutrons with Newton laws, and handle low energy scattering (E < 100 meV)
- Suitable for neutron scattering studies, e.g. SANS, diffraction, imaging
- Can model background from scattering on surrounding materials
- Can use neutron from MCNP with PTRAC card

---
What McStas does NOT
- Can not handle high energy moderation
- Not appropriate to estimate fast neutron background and g
- Not appropriate for in-pile design (shielding, beam tubes)

---
Schematic neutron propagation
McStas
n

---
Schematic neutron propagation
McStas
n
Neutron ray/package:
Weight (p): # neutrons (left) in the package
Coordinates (x,y,z)
Velocity (vx,vy,vz)
Spin (sx,sy,sz), Time (t)

---
Schematic neutron propagation
McStas
n
Components: Here the neutron physics (Bragg law) happen, neutron weight adjusted according to scattering probabilities etc (Monte Carlo is here).

---
Schematic neutron propagation
McStas
n
Instrument: positioning + transformation between sequential component coordinate systems, e.g. neutron source, crystal, detector.

---
McStas grammar
Instruments are defined from a text file. General syntax is based upon C.
Basic syntax:
DEFINE INSTRUMENT name(parameter1=value1, …)
DECLARE %{ /* global variables */
%}
INITIALIZE %{ /* code executed when starting */
%}
TRACE	/* sequence executed for each neutron event */
COMPONENT InstanceName=component(parameters...)
AT (position) RELATIVE reference
ROTATED (orientation) RELATIVE reference
...
END
Can be changed from cli and GUI (e.g. scans)

---
McStas components
Sources (neutrons)
Continuous (reactor), Pulsed
Moving optics
Choppers (disk and Fermi), velocity selectors, phase space transformers
Static optics
Guides, mirrors, benders, lenses, collimators, slits, filters, monochromators
Samples/materials
Single crystals, liquids, gas, polymers, hard spheres
Detectors
Histogram and event monitors, gas detectors
Total 190+ components, 90+ examples, manuals, tutorials...

---
Neutron optics: monochromators (primary spect.)
Monochromators are used to extract a
sharp neutron energy distribution from a white beam.
Rely on Bragg's law.
Use single crystal assembly, with focusing geometry.
Size: Typically 20x20 cm
Design and characterisation are eased using simulation,
intensity vs. curvature radius,
thickness of blades
rocking curve (reflectivity)
scattering from the mechanics (generated background)
choice of crystals
Cu, Ge, Si, C (graphite)
CuMnAl, CoFe (pol.)

---
Source: Generating neutron events
Neutron events may be currently generated from:
A black body (Maxwellian distributions)
Measured flux/divergence distributions
MCNP and Tripoli (nuclear reactor simulation codes) event files
Pulsed sources (SNS, ESS, ISIS, J-PARC...)
Other neutron generators are in principle easy to write
(e.g. from GEANT, FLUKA, ...)
top
 n = (R, v, t, s, p)
side

---
Virtual experiments: definition
Virtual experiments
=
Instrument simulation
⊗
Realistic Sample model
=
Neutron flight simulator
and then we play with it without breaking the instrument and sample.
E. Farhi et al, J. of Comp. Phys. 228 (2009) 5251
E. Farhi and P. Willendrup, Collection SFN 12 (2011) 303
E. Farhi et al., J. Neut. Res., 18 (2013)

---
Benefits from a virtual experiment
Benefits:
The resolution from the instrument is implicitly convolved with the sample, without analytical integration
The 'spurious' effects from the instrument can be included
Treat absorption in the sample (self attenuation=2nd extinction)
Treat coherent/incoherent scattering
May include multiple scattering (depends on the sample component)
May model the measurement background
Requirements:
Need as accurate instrument description as possible
Use proper sample component/kernel
Give accurate data to the sample component (experiment, MD, …)
Be critical regarding the results (it's so easy to get rubbish)

---
McStas: available sample components
Most instrument components are 'easy' to implement.
The samples are often more complex.
Sample geometry: box, cylinder, sphere, PLY/OFF file

---
What can be done at TRIGA PUSPATI

---
Neutron diffraction
- Bragg law: 2d sin q = nl coherent scattering
- We send a single l and get diffraction rings at angles q for each d spacing.
- In a cubic crystal d=a/√(h2+k2+l2)
- q = asin(nl√(h2+k2+l2)/2a)
- If l > 2a, no Bragg diffraction can occur
- Cold beam (e.g. SANS@PUSPATI) no diffraction → Bragg edge

---
Diffraction example
templateSANS
l=6 +/- 0.5 Å
Latex colloid solution r=100 Å
Detector 128*128 (30 cm)
Similar with l=2 (thermal), r=50
TemplateDIFF
l=6 Å, PG(002) monochromator

---
What to use neutrons for ?
- I will describe a set of simple instruments that can make use of neutrons for studying of materials
- Only use basic 'optics' components
- In principle, we can install such instruments on a TRIGA reactor

---
SANS
- Should better use 'cold' neutrons with E < 5 meV
- Scattering obtained from structure on length scales in the material (low angle diffraction).
- Q ~ 4p/l sin(q) ~ 2pr/(lL) with L=sample-detector and r=radius of scattering ring on detector
- l should be 'rather' monochromatic and cold/thermal
- Q range for SANS@RTP 0.01-0.1 Angs-1
- Plot I(Q2), get RG

---
Diffraction: Laue
- Uses a white incoming beam (or band) → full flux
- Diffracts on a crystal sample → allow to get its structure
- Needs a 'small' divergence/beam section
- Needs an image plate/PSD to acquire image
- Adapted to thermal wavelength
- Easy to get qualitative but accurate data analysis is hard

---
Diffraction : powder
- Requires a monochromatic beam
- Requires a movable detector around sample or PSD
- Diffracts neutron on powder → give its structure
- Adapted to thermal wavelength
- Applications for industry: metallurgy, strain/stress

---
Neutrons from TRIGA
- 1MW nominal power ~ 1/100e of ILL
- Flux is mostly thermal, with 1/100e fast/epithermal.
- Should allow to perform diffraction experiments within a day
- Tangential tubes as good as the radial ones, less g
Radial tube, from Teruel,
Rizwan-uddin PHYSOR2004

---
Possibilities at TRIGA PUSPATI
- Use central thimble door plug to get maximum flux
- Use tangential tubes to reduce g-level for NR/Laue
- Upgrade SANS monochromator (re-align)
- Install a powder diffractometer using one monochromator blade or velocity selector
- Install movable block to allow changing take-off

---
Tutorials
Source-Tube
Monochromator
Sample-Detector

---
McStas Installation Party
<mcstas.org/download/>
Windows:
Use Installer (32bits – OK on 64), press Next until the End. Logout/Login.
Will make use of Matlab if present at install (plotting).
Linux:
Use Debian package (32 and 64 bits) on Ubuntu et al.
cd /etc/apt/sources.list.d
sudo wget http://packages.mccode.org/debian/mccode.list
sudo apt-get update ; sudo apt-get install mcstas-suite
Recommended 3rd party:
OpenMPI, freewrl from <www.freewrl.org> or view3dscene
MacOSX: we supply a dmg, which requires Xcode (gcc)+Xquartz.
Any machine, without installation:
Get our LiveDVD at <http://mcstas.org/ubuntu/>
and <http://www.ill.eu/instruments-support/useful-tools/>

---
McStas: Help me !
<www.mcstas.org> RTFM
<mcstas-users@mcstas.org> quick answer guaranteed !
McGUI Help menu (right top side)
→ Manuals, Component and example instrument list/doc.
McGUI Neutron Site menu: Example instruments listed
→ You will probably find an instrument which matches your needs, as a starting point.

---
McStas: Getting started
Windows and MacOSX: click on the McStas/McGUI Desktop Icon
LiveDVD: select menu Applications/Education/McStas
Command line: mcgui, and for geeks mcrun, mcplot, mcdisplay

---
Exercise 1: Source and Monitor
Start the McStas GUI: McGUI
Select Neutron Site/Templates/template (test)
Click on the Edit button. Remove the Par1=0 parameter.
Position the cursor in the TRACE after the Origin component.
From the Insert menu, select Source/Source_gen component
Insert a 'source' instance name, a 15x15 cm² geometry, focusing on a f=12 cm at 1.35 m, shooting l=4±3.5 Å neutrons, and position it at the (0,0,0) relative to the Origin. Use I1=1e11, T1=300 (thermal, TRIGA).
Insert a 'monitor' instance : 12x12 cm² Monitor_nD with options="auto lambda bins=50" at 1.3 m (along Z) from the source.
Save your instrument as Source.instr,
NOT in Documents and Settings
(Windows does not handle spaces in file names correctly).
Click on the Run button, indicate the directory to save to, e.g. Source and press Start.

---
Warning : in the following nasty neutrons will be shot
Virtual radiation hazard
Trespassers will be shot !
Survivers will be shot again !

---
Exercise 2: Monochromator
- In the DEFINE INSTRUMENT line, define lambda=4 and DM=3.355
- At 50 cm from the previous l-monitor, add an Arm
- On this Arm, add a Monochromator component h*w=9*11 cm, DM=DM, and rotate it around Y-axis with angle asin(lambda/(2*DM))*RAD2DEG
- Still on the Arm, define a second Arm rotated by twice the previous angle
- At 50 cm from the last Arm, place a Monitor_nD sensitive to wavelength
- Save simulation as Monochromator.instr and run it

---
Exercise 3: Sample and Detector
- At 2 m flight path, place a Sans_spheres 1 cm3
- At 3 m away place a PSD 30 cm2 128 bins
- Save simulation as RTP_SANS_0.instr and run it

---
Exercise 4: Be-filter
- In between the source and the 1st l-monitor, install a PowderN with reflection file as “Be.laz” 15cm side.
- Save instrument RTP_SANS_1.instr and run it

---
Exercise 5: background from sample environment
- Around the sample, install a SiO2 or V container, thickness 50 mm, with PowderN(concentric=1). Place a COPY of this component after the sample with concentric=0.
- Copy the last PSD and set a condition to only detect the scattering on the container. This requires to define in DECLARE a 'flag' variable, and set it flag=SCATTERED in an EXTEND block in the container.
- Save instrument RTP_SANS_2.instr and run it

---
Exercise 6: Radiography
- Get the initial Source.instr (Exercise 1) and save it as Radiography.instr
- Just before the l-monitor, place a PowderN with geometry=”socket.off”, made of copper 'Cu.laz'
- COPY the l-monitor as an XY monitor, 512x512 pixels on 20x20 cm.
- Save and run instrument.