## Slide 1: McStas Union components
What they are and how to use them
PRESENTED BY Mads Bertelsen
This project has received funding from the European Union’s Horizon 2020 research
and innovation programme under grant agreement No. 823852

## Slide 2: Introduction
Difficulties with realistic samples
Sample holders with complicated geometry
Consists of many different materials
No clear order in which neutrons would pass through
Could have co aligned crystals
Twinned crystals
It could all be in a sample environment
Photo by Pia Ray Jensen
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 3: Physics
Modular physics description
Combine simple physical processes
    Incoherent scattering
    Powder Bragg scattering
    Single crystal Bragg scattering
    Simple phonon
    …
Create material definitions by combining an arbitrary number of these processes and an absorbation cross section
Incoherent_process
Powder_process
Incoherent_process
Single_crystal_process
Incoherent_process
Single_crystal_process
NCrystal_process
Inelastic sample
Al
Sample
Processes
Materials
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 4: Physics
Modular physics description
Incoherent_process
Powder_process
Al
Processes
Materials
COMPONENT Al_incoherent = Incoherent_process( sigma = 4*0.0082, packing_factor=1, unit_cell_volume = 66.4) AT (0,0,0) ABSOLUTE
COMPONENT Al_powder = Powder_process( reflections = "Al.laz") AT (0,0,0) ABSOLUTE
COMPONENT Al = Union_make_material( my_absorption = 100*4*0.231/66.4, process_string = “Al_incoherent,Al_powder”) AT (0,0,0) ABSOLUTE
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852
my [1/m] =
cross section per unit cell
unit cell volume
Absorption given as inverse penetration depth

## Slide 5: Geometry
Modular geoemtry
Construct the desired geometry from simple basic shapes
    Sphere
    Cylinder
    Box
    Cone
    CAD model (stl files)
  Assign each geometry a material
Incoherent_process
Powder_process
Incoherent_process
Single_crystal_process
Incoherent_process
Single_crystal_process
NCrystal_process
Inelastic sample
Al
Sample
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 6: Geometry
Priority
Each geometry is given a priority
When two geometries overlap, the overlapping region has the material of the highest priority
This allows the user to create complex geometries
Vanadium priority = 5.1
Aluminium priority = 8.2
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 7: Geometry
Priority
Each geometry is given a priority
When two geometries overlap, the overlapping region has the material of the highest priority
This allows the user to create complex geometries
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 8: Geometry
Modular geometry
Al
COMPONENT cryostat_shell = Union_cylinder( radius = 0.15, height = 0.4, priority = 10, material_string = "Al") AT (0,0,0) RELATIVE target ROTATED (0,0,0) RELATIVE target
COMPONENT cryostat_vacuum = Union_cylinder( radius = 0.147,height = 0.39, priority = 11, material_string = "Vacuum") AT (0,0,0) RELATIVE target ROTATED (0,0,0) RELATIVE target
Vacuum
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 9: Union master
Where the simulation actually happens
All components discussed doesn’t actually perform any simulation
Process and geometry components describe the system to be simulated
The Union_master component performs the simulation
A Union_master must be inserted, and will simulate all Union geometry components defined so far
No inputs are necessary, as all the information is already in the processes and geometry
COMPONENT master = Union_master() AT (0,0,0) ABSOLUTE
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 10: Union master
Overview of a Union setup
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 11: Introduction
How does this improve the situation?
Photo by Pia Ray Jensen
Sample holders with complicated geometry
Consists of many different materials
No clear order in which neutrons would pass through
Could have co aligned crystals
Twinned crystals
It could all be in a sample environment
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 12: Multiple scattering
Logic in McStas instrument
Multiple scattering handled in Union_master component
Neutron handed back to instrument component sequence
Instrument file
Simulated 3D space
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 13: Multiple scattering
Instrument file
Simulated 3D space
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852
Logic in McStas instrument
Multiple scattering handled in Union_master component
Neutron handed back to instrument component sequence
Ray can go to geometries in any order

## Slide 14: Multiple scattering
Instrument file
Simulated 3D space
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852
Logic in McStas instrument
Multiple scattering handled in Union_master component
Neutron handed back to instrument component sequence
Ray can go to geometries in any order
Internal logic network reduce number of intersection calculations, improving execution speed

## Slide 15
2
Demonstration

## Slide 16: Demonstration
log(I)
5 meV beam
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 17: Demonstration
log(I)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 18: Demonstration
log(I)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 19: Demonstration
log(I)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 20: Demonstration
log(I)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 21: Demonstration
log(I)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 22: Demonstration
log(I)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 23: Demonstration
log(I)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 24: Demonstration
log(I)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 25: Demonstration
log(I)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 26: Demonstration
log(I)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 27: Logger components
Recording information during simulation
Loggers can be used to understand what is going on during simulation
Can either log everything, or be attached to a geometry or process
Physics
Geometry
Logging
Incoherent_process
Powder_process
Incoherent_process
Single_crystal_process
Incoherent_process
Single_crystal_process
NCrystal_process
Inelastic sample
Al
Sample
  Loggers Records at scattering event
  Absorption loggers Records at absorption event
  Can be attached to: Geometries Processes
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 28: Logger components
Recording information during simulation
List of loggers
  Union_logger_1D
  Union_logger_2DQ
  Union_logger_2D_kf
  Union_logger_2D_kf_time
  Union_logger_2D_space
  Union_logger_2D_space_time
  Union_logger_3D_space
List of absorption loggers
  Union_abs_logger_1D_space
  Union_abs_logger_1D_space_event
  Union_abs_logger_1D_space_tof
  Union_abs_logger_1D_space_tof_to_lambda
  Union_abs_logger_2D_space
  Union_abs_logger_event
All loggers record something at scattering or absorption
They can all be set to only log certain scattering order

## Slide 29: Logger components
Recording information during simulation
Need to understand the simulation
Record information during scattering
Here spatial distribution of scattered intensity from above
COMPONENT scattering_zx = Union_logger_2D_space( D_direction_1="z", D1_min=-0.15, D1_max=0.15, n1=300, D_direction_2="x", D2_min=-0.15, D2_max=0.15, n2=300, filename="scattering_zx.dat") AT (0,0,0) RELATIVE sample_position

## Slide 30: Logger components
Recording information during simulation
A specific scattering order can be shown
Improves understanding of what occured
1
2
3
All

## Slide 31: Logger components
Recording information during simulation
Here the scattering vector is recorded
Visible Bragg peaks and Debye Scherrer cones

## Slide 32: Logger components
Recording information during simulation
1
2
3
All
A specific scattering order can be shown
Improves understanding of what occured

## Slide 34: Conditional components
Limiting logger components to record interesting neutrons
Wish to understand how individual background features arose
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 35: Conditional components
Limiting logger components to record interesting neutrons
Conditional components set up some condition upon the final neutron, such as if it hits a certain area
Conditional components modify existing loggers with target_loggers
Can specify many loggers with comma separated list
Current conditionals
    Union_conditional_PSD
    Union_conditional_standard
COMPONENT scattering_zx = Union_logger_2D_space( D_direction_1 = "z", D1_min = -0.15, D1_max = 0.15, n1 = 300, D_direction_2 = "x", D2_min = -0.15, D2_max = 0.15, n2 = 300, filename = "scattering_zx.dat") AT (0,0,0) RELATIVE sample_position
COMPONENT conditional_psd = Union_conditional_PSD(
xwidth = 0.02, yheight = 0.02,
time_min = 2E-6, time_max = 8E-6
target_loggers = ”scattering_zx”)
AT (0,0,1) RELATIVE sample_position

## Slide 36: Conditional components
Limiting logger components to record interesting neutrons
Wish to understand how individual background features arose
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 37: Conditional components
Limiting logger components to record interesting neutrons
Wish to understand how individual background features arose
Select subset of output to be recorded in loggers using Union conditionals
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 38: Conditional components
Limiting logger components to record interesting neutrons
Can limit the events that are recorded to the logger using conditionals
Here only rays that contribute to the chosen background problem is seen
Spatial distribution of scattered intensity
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 39: Conditional components
Limiting logger components to record interesting neutrons
The different scattering orders makes it easier to draw conclusions
The sample is clearly involved
1
2
3
All

## Slide 40: Conditional components
Limiting logger components to record interesting neutrons
Scattering vectors of rays that contribute to the chosen background problem
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852

## Slide 41: Conditional components
Limiting logger components to record interesting neutrons
1
2
3
All
The different scattering orders makes it easier to draw conclusions
Single crystal Bragg peak to powder Debye Scherrer cone

## Slide 43: Summary
Union components allow simulation of complex physics and geometry
Full multiple scattering simulation provides surprising level of detail
The modular nature makes it easier to expand
    New geometry with a geometry component (Master project contributed cone and CAD)
    New process component to add new physics
Full tutorial available in McStasScript format!

## Slide 44: Thanks for your attention
This project has received funding from the European Union’s Horizon 2020 research
and innovation programme under grant agreement No. 823852