## Slide 1: guide_bot
Mads Bertelsen
Post Doc at DMSC in DRAM group led by Thomas Holm Rod
European Spallation Source ERIC
4/6 2021 @ PNPI

## Slide 2: Introduction
Worked with McStas last 9 years, now McStas developer
PhD from University of Copenhagen under Kim Lefmann in 2017
Now Post Doc at ESS Data Managment and Software Centre, funded by PaNOSC and HighNESS
Writes software, happy when someone wants to use it and learn about my projects!
Who am I?
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852
guide_bot
Union components
McStasScript
Automatic guide optimization given requirements and overall geometry (MATLAB)
Modular samples, multiple scattering within McStas
Flexible McStas Python API
Mads Bertelsen

## Slide 3: Introduction
guide_bot talk, shorter than planned
break
Union components and simulating sample environments
break
McStasScript and oppertunity to try online!
Slight restructuring for today!
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 823852
guide_bot
Union components
McStasScript
Automatic guide optimization given requirements and overall geometry (MATLAB)
Modular samples, multiple scattering within McStas
Flexible McStas Python API
Mads Bertelsen

## Slide 4: guide_bot
Guide design workflow
General problem, provide the best guide for given beam requirements
Guide design is a laborious process and many alternative solutions exists
In many cases the amount of work involved means only few solutions are investigated
HighNESS is funded by the European Framework for Research and Innovation Horizon 2020, under grant agreement 951782
Beam requirements and constraints
(figure of merit)
Think of guide geometries
Simulate, optimize, characterize
Compare solutions

## Slide 5: guide_bot
guide_bot was my attempt to provide a tool that will ease the process of guide design
The first version of guide_bot was written in 2013 using MATLAB
    Simple system for describing guide geometry
    Writes McStas instrument file corresponding to the geometry
    Sets up numerical optimization using iFit written by Emmanuel Farhi
    Runs on ESS DMSC cluster
    Produces figures describing the guide performance
This first version of guide_bot is sadly obsolete
New version is being written in python
iFit
Bertelsen, M. (2017). The automatic neutron guide optimizer guide_bot.
Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, 830, 313-324. https://doi.org/10.1016/j.nima.2017.06.012
https://github.com/mads-bertelsen/guide_bot

## Slide 6: guide_bot
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations
Description of desired beam
Instrument length
Facility information
Computing options
Coating description (not optimized)

## Slide 7: guide_bot
S
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 8: guide_bot
S S
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 9: guide_bot
S S E S
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 10: guide_bot
Module | Description
S | Straight guide
E | Elliptic guide
P | Parabolic guide
G | Gap
C | Curved guide
K | Kink
Selene | Selene guide system
Slit | Slit
M | Monochromator
Contributed by Leland Harriger, NIST, USA
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 11: guide_bot
Code | Function
length | Length of the module
start | Start of the module
StartWidth | Start width of a module
StartHeight | Start height of a module
EndWidth | End width of a module
EndHeight | End height of a module
S C(start=6) S(maxlength=20)
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 12: guide_bot
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 13: guide_bot
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 14: guide_bot
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 15: guide_bot
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 16: guide_bot
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 17: guide_bot
ESS moderator height scan
Often the beam requirements are not well defined
”How large a sample would be reasonable before loosing brilliance transfer?”
Scan beam requirements and optimize all guides for value
Scan dimensions Moderator dimensions Divergence requirement Sample size
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 18: guide_bot
ESS moderator height scan
Scan dimensions Moderator dimensions Divergence requirement Sample size
Used in connection with ESS moderator decision
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 19: guide_bot
ESS moderator height scan
C-SPEC results
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations

## Slide 20: guide_bot
ESS moderator height scan
Input Job description
Geometry string
Optimization
Optimization of the guide
Output
Guide characterization
Scan of optimizations
Guide start 2 m from source

## Slide 21: guide_bot
CoatingWriter expansion
Coating optimization add-on to guide_bot by Martin Olsen (KU)
Can optimize coating / geometry simultaneously or sequentially
Olsen, M. A., Bertelsen, M., & Lefmann, K. (2018). Optimizing neutron guides: CoatingWriter.
Journal of Neutron Research, 20(4), 137-139. https://doi.org/10.3233/JNR-180098
https://github.com/MartinAOlsen/CoatingWriter

## Slide 22: guide_bot
Summary
Performed more than 20000 guide optimizations
Tens of millions of McStas simulations
Designed guides for several ESS instruments
Used at PSI and NIST
Now too difficult to install / maintain
3000
2000
1000
Guide optimizations per month 2013-2015

## Slide 23: guide_bot
Progress on python version
Motivation for making python version of guide_bot
    Want to avoid the requirement of MATLAB license
    Want to provide better customization of source / figure of merit
    Object oriented design more suitable for the task
    Can use McStasScript as McStas API and python dependencies for optimization
    Can provide a package that is easier to install and more reliable
HighNESS is funded by the European Framework for Research and Innovation Horizon 2020, under grant agreement 951782

## Slide 24: guide_bot
Python guide_bot example
HighNESS is funded by the European Framework for Research and Innovation Horizon 2020, under grant agreement 951782

## Slide 25: guide_bot
Python guide_bot example
HighNESS is funded by the European Framework for Research and Innovation Horizon 2020, under grant agreement 951782

## Slide 26: guide_bot
Python guide_bot example
HighNESS is funded by the European Framework for Research and Innovation Horizon 2020, under grant agreement 951782

## Slide 27: guide_bot
Python guide_bot example
HighNESS is funded by the European Framework for Research and Innovation Horizon 2020, under grant agreement 951782

## Slide 28: guide_bot
Python guide_bot example
HighNESS is funded by the European Framework for Research and Innovation Horizon 2020, under grant agreement 951782
Defines custom parameters
Sets min / max length
Use of our custom
parameters

## Slide 29: guide_bot
Python guide_bot example
Writes project folder which should be uploaded to cluster
Contains script for running all optimizations
After jobs complete the data can be downloaded
HighNESS is funded by the European Framework for Research and Innovation Horizon 2020, under grant agreement 951782

## Slide 30: guide_bot
Progress on python version
Exploration of the data
    Show jupyter notebook live demo

## Slide 31: guide_bot
Progress on python version
Additional new features in python version
    User defined constraints
    Scan as many dimensions as desired
    Have analysis runs for as many moderators as desired
    Easier addition of sources, figure of merit, clusters, guide elements, …
Features not yet implemented in python version
    System to handle loosing line of sight
    More guide elements (only straight, elliptic and gap available now)
    General system handling reflectivity options
    Coating optimization
    Plotting of the finished guide
    Nice report for each optimized guide

## Slide 32: guide_bot
Conclusions
The process of guide design can be made significantly easier with a tool like guide_bot
The first version of guide_bot had external users and arguably high impact
My apologies for not maintaining the software
New python version on the way, hope this will satisfy the needs of the community
More professional software, easier to contribute / collaborate, easier to install and truly open source
https://git.esss.dk/highness/guide_bot

## Slide 33: Thanks for your attention